UNIT I

CLUTCH AND GEAR BOX

TRANSMISSION SYSTEM

Chief function of the device is to receive power at one torque and

angular velocity and to deliver it at another torque and the corresponding

angular velocity.

LAYOUT OF AUTOMOBILE POWER TRANSMISSION SYSTEM

REQUIREMENTS OF TRANSMISSION SYSTEM

1.  To provide for disconnecting the engine from the driving wheels.

2.  When  the  engine  is  running,  to  enable  the  connection  to  the  driving

wheels to be made smoothly and without shock.

3.  To  enable  the  leverage  between  the  engine  and  driving  wheels  to  be

varied.

4.  It must  reduce  the drive-line speed from  that  of  the engine  to  that  of

the driving wheels in a ratio of somewhere between about 3:1 and 10:1

or more, according to the relative size of engine and weight of vehicle.

5.  Turn the drive, if necessary, through 90° or perhaps otherwise re-align

it.

6.  Enable the driving wheels to rotate at different speeds.

7.  Provide for relative movement between the engine and driving wheels.

AT2301 Automotive Transmission

CLUTCH

The  clutch  is  housed  between  the  engine  and  transmission  where  it

provides  a  mechanical  coupling  between  the  engine's  flywheel  and  the

transmission  input  shaft.  The  clutch  is  operated  by  a  linkage  that  extends

from  the  passenger  compartment  to  the  clutch  housing.  The  purpose  of  the

clutch  is  to  disconnect  the  engine  from  the driven  wheels  when  a  vehicle  is

changing gears or being started from rest.

Disengaging the clutch separates the flywheel, the clutch plate and the

pressure  plate  from  each  other.  The  flywheel  is  bolted  to  the  end  of  the

crankshaft  and  rotates  with it.  The clutch  plate is splined  to the  gearbox  in

order  for  both  to  rotate  together  and  the  pressure  plate  clamps  the  clutch

plate to the flywheel. When the pressure is released by depressing the clutch

pedal,  the  crankshaft  and  gearbox  input  shaft  rotate  independently.  When

the foot is taken off they rotate as one.

REQUIREMENTS OF A CLUTCH

The clutch must

1.  Pick up its load smoothly without grab or clatter.

2.  Have a driven disc of low moment of inertia to permit easy shifting.

3.  Damp out any vibration of the crankshaft to prevent gear clatter.

4.  Require little pedal pressure to operate it.

5.  Be easy to adjust and service.

6.  Be cheap to manufacture.

BASIC PRINCIPLE OF THE FRICTION TYPE CLUTCH

To  understand the  working principle of  clutch,  let’s  take two  sanding

discs,  first one driven  by  a  power  drill corresponds  to  the  flywheel  of  a car,

driven by the engine. If a second sanding disc is brought into contact with the

first, friction makes it revolve too but more slowly. But when the second disc

pressed  against  the  first  disc  which  is  connect  to  the  power  drill,  as  the

pressure increases the two  discs revolve as  one.  This is how a  friction clutch

works.

BASIC PRINCIPLE OF THE FRICTION TYPE CLUTCH

TYPES OF CLUTCHES

MULTI COIL SPRING SINGLE PLATE CLUTCH

CONSTRUCTION

A typical clutch actuated  by a number of  coil  springs on  a pitch circle

nears the  periphery is  shown. The  driven shaft  which normally  is a forward

extension  of  gearbox  primary  shaft  is  supported  at  its  front  end  in  ball

bearing in a hole in the centre of flywheel web, which is spigot and bolted on

to a flange at the rear end of the crankshaft.

In  this  clutch,  the  coil  springs  force  the  pressure  plate  forwards  to

clamp  the  driven  plate  between  it  and  the  rear  face  of  the  flywheel.  Three

lugs  extend  rearwards  from  periphery  of  pressure  plate  both  to  rotate  the

pressure  plate  and  to  cause  it  to  rotate  with  the  rest  of  the  assembly.  The

driven plate of  course is splined onto the shaft.

There  are  three  release  levers  pressing  the  coil  springs  at  the  outer

end. The inner  ends  of the  levers  can be  forced  forward by means of  thrust

bearing made of graphite  and slide along  the clutch shaft when  clutch pedal

is depressed. The driven plate mounted between flywheel and pressure plate

makes  the clutch  shaft  to rotate to  transmit  power.  It  has the  clutch  facing

made of friction materials around the periphery of disc.

WORKING

When  the  clutch  is  engaged,  the  clutch  plate  is  gripped  between  the

flywheel  and  pressure  plate.  The friction  linings  are  on  both  sides of  clutch

plate.  Due to  friction between flywheel,  clutch plate  and pressure  plate,  the

clutch  plate  revolves  with  the  flywheel.  As  clutch  plate  revolves  the  clutch

shaft also revolves. Thus, engine power is transmitted to the clutch shaft.

When  the  clutch  pedal  is  pressed  the  pressure  plate  moves  back

against the  spring force and clutch plate  becomes free between flywheel and

pressure plate. Thus flywheel remains rotating as long as the clutch pedal is

pressed,  the  clutch  is  said  to  be  disengaged  and  clutch  shaft  speed  reduces

slowly and finally it stops rotating.

DIAPHRAGM SPRING SINGLE PLATE CLUTCH

Diaphragm  spring  pressure  plate  assemblies  are  widely  used  in  most

modern  cars.  The  diaphragm  spring  is  a  single  thin  sheet  of  metal  which

yields  when  pressure  is  applied  to  it.  When  pressure  is  removed  the  metal

springs back to its original shape. The centre portion of the diaphragm spring

is slit into numerous fingers that act as release levers. During disengagement

of the clutch the fingers are moved forward by the release bearing.

The spring pivots over the fulcrum ring and its  outer rim moves away

from  the flywheel. The retracting spring pulls  the pressure  plate away  from

the  clutch  plate  thus  disengaging  the  clutch.  When  engaged  the  release

bearing  and  the  fingers  of  the  diaphragm  spring  move  towards  the

transmission. As the diaphragm pivots over the pivot ring its outer rim forces

the pressure plate against the clutch disc so that  the clutch  plate is engaged

to the flywheel.

ADVANTAGES OF DIAPHRAGM SPRING CLUTCH

1.  It is more compact than other designs.

2.  It  is  easier  to  balance  rotationally  and  is  less  subjected  to  unwanted

effects due to centrifugal force at high rotational speeds.

3.  It gives uniformly distributed pressure on pressure plate.

4.  It needs no release levers.

5.  Minimum effort is sufficient to disengage the clutch.

6.  It  provides  minimum  number  of  moving  components  and  hence

minimum internal friction is experienced.

7.  This is  very commonly  used in cars, light Lorries  and  mini  trucks but

is not much used in heavy vehicles

MULTIPLATE CLUTCH

The  multi-plate  clutch  is  an  extension  of  single  plate  type  where  the

number  of frictional and  the metal plates are  increased. The increase in the

number  of  friction  surfaces  obviously  increase  capacity  of  the  clutch  to

transmit torque, the size remaining fixed. Alternatively, the overall diameter

of  the  clutch  is  reduced  for  the  same  torque  transmission  as  a  single  plate

clutch.  This  type  of  clutch  is,  used  in  some  heavy  transport  vehicles,  in

epicyclic  gearboxes  and  racing  cars  where  high  torque  is  to  be  transmitted.

Besides,  this  finds  applications  in  case  of  scooters  and  motorcycles,  where

space available is limited.

Extension  of  flywheel  is  a  drum;  which  on  its  inner  circumference  is

splined  to  carry  a  number  of  thin  metal  plates.  These  must  consequently

revolve with  drum but are able  to  slide axially. Interleaved with these  outer

plates are a  number of inner plates that are splined to  an inner  drum which

is coupled rotationally to the gearbox shaft.

This  drum  is  supported  on  a  spigot  extension  of  crankshaft.  Between

the web  of inner drum and sleeve in inner drum  is  a  strong coil  spring.  The

inner  drum  is  thus  pressed  to  left  being  provided  with  a  flange  it  squeezes

the  inner  and outer plates together so that friction between  them  transmits

driving torque from outer to inner drum.

The  clutch  is  disengaged  by  pulling  inner  drum  right  against  spring

force.  The  plates  of  multi-plate  clutch were  at  one  time  made  alternately  of

steel  and  phosphor  bronze  but  now  are  all  of  steel  or  one  set  may  be  lined

with  a  friction  material.  With  metal  contact  lubrication  is  essential  and  so

clutch is made oil-tight and  partly filled  with  oil. The oil  tends  to  make  the

plates drag when clutch is disengaged and so some mean should be provided

to avoid this drag.

DRY MULTIPLATE CLUTCH

Multi  plate  clutches  are  also  made  to  work dry,  without  any  oil.  The

driving  plates  are  then  lined  on  each  side  with  a  friction  fabric.  In  such

clutches,  the  driving  plates  are  sometimes  carried  on  a  number  of  studs

screwed  into  the  web  of  flywheel  in  the  same  way  as  the  outer  plate  of  a

Single  Plate  Clutch is carried.  This  construction  is  inconvenient  when oil  is

used. Several small springs can be used instead of a single spring.

AUTOMATIC CLUTCH

Many attempts have been made to produce motor vehicles that can be

controlled  by  the  accelerator  pedal  and  brakes  only.  This  can  be  done  in

several  ways.  A  centrifugal  clutch  which  automatically  disengages  itself

when the speed falls below and which re-engages when the speed rises above

some predetermined values may be used. Alternatively, a fluid coupling, fluid

torque converter may be employed.

CEN TRIFUGAL CLUTCH

In this type of clutches  the springs are eliminated altogether and only

the  centrifugal  force  is  used  to  apply  the  required  pressure  for  keeping  the

clutch in engagement position.

The  advantage  of  the  centrifugal  clutch  is  that  no  separate  clutch

pedal  is required.  The  clutch  is  operated  automatically  depending  upon  the

engine speed. This means that car can be stopped in gear without stalling the

engine.  Similarly  while  starting,  the driver  can first select the gear,  put the

car  into  the  gear  and  simply  press  the  accelerator  pedal.  This  makes  the

driving operation very easy.

Figure shows a schematic diagram of a centrifugal clutch. As the speed

increases, the  weight A fly off,  thereby operating  the bell  crank  lever  B  that

presses  the  plate  C.  This  force  is  transmitted  to  the  plate  D  by  means  of

springs E.  The  plate D  containing  friction  lining  is thus  pressed against the

flywheel F thereby engages the clutch. Spring  G  serves  to  keep  the  clutch

disengaged  at  low  speed  say  500  rpm.  The  stop  H  limits  the  amount  of

centrifugal force.

The  operating  characteristics  of  this  type  of  clutch  will  be  then  as

shown  in  figure.  Force  P  is  proportional  to  the  centrifugal  force  at  a

particular speed, while force Q exerted by spring G is constant at all speeds.

The  firm  line  in  the  figure  shows  that  net  force  on  the  plate  D  for  various

engine speeds. At the upper end the curve is made f lat by means of stop H.

SEMI CENTRIFUGAL CLUTCH

It uses both  centrifugal  and spring force  for  keeping  it  in  an engaged

position. The springs are designed  to transmit torque at normal speed, while

centrifugal  force  assists  in  torque  transmission  at  high  speed.  This  clutch

consists  of  three  hinged  and  weighted  levers  and  three  clutch  springs

alternately arranged at equal spaces on the pressure plate. At low speeds the

springs  keep  the  clutch  engaged  and  the  weighted  levers  do  not  have  any

pressure on pressure plate. At high speeds when power transmission is high,

weights fly off and the levers also exert pressure on plate, keeping the clutch

firmly engaged.

When the speed decreases the weights do not exert any pressure on the

pressure plate. Only spring pressure is exerted on pressure plate which keeps

the clutch engaged. An adjusting screw is provided at the end of  the lever by

means  of  which  the  centrifugal  force  on  pressure  plate  can  be  adjusted.  At

low  speeds  pressure  on  the  spring  is  sufficient  to  transmit  the  torque

required.

However  at  high  speeds,  the  centrifugal  force  due  to  weight  moves

about  the fulcrum thereby pressing the  pressure plate.  The centrifugal force

is  proportional  to  the  square  of  speed  so  that  adequate  pressure  level  is

attained.

Graph  shows  the  variation  of  force  on  the  pressure  plate  as  speed

increases. At low speeds spring along applies the force on the pressure plate.

But when speed of the engine raises the centrifugal force also applied by the

weights.

TORQUE CAPACITY OF A SINGLE PLATE CLUTCH

Assume the clutch has a single disc and it may be coil spring clutch or

diaphragm spring clutch.

Area of each friction surface of the disc A  =  /4 ( Do

– Di

)

2

2

Normal force applied by the pressure springs =  /4 ( Do

– Di

) p

2

2

Net axial force applied by pressure springs  =  /4 ( Do

– Di

) p

Kgf

2

2

mech

Frictional force applied to each frictional face =  /4 ( Do

– Di

) µ p

Kgf

2

2

mech

Torque due to both surface  =  /2 ( Do

– Di

) µ p

R

Kgf-cm-------1

2

2

mech

m

Where

µ = coefficient of friction,

p = permissible unit pressure on friction surfaces

Di = inner outer diameter of disc

Do = outer diameter of disc

R

= mean radius of the friction surface in cm

m

R

= coefficient of reserve (R

value = 1.4)

F

F

= coefficient of mechanical efficiency (

value = 0.85)

mech

mech

Consider a small element at radius ‘r’ and of thickness ‘dr’.

Area of the element a        = 2 rdr  cm

2

Normal force          = 2 rdr p Kgf

Frictional force          = 2 rdr p µ Kgf

Torque transmitted by each elemental area  = 2 r2 dr p µ Kgf-cm

Torque transmitted by each friction surface  =

2 r

dr p µ Kgf-cm

2

= 2  µ p [ r

/ 3 ] Kgf-cm

3

= 2  µ p [ D

D

/ 8x3 ] Kgf-cm

O3_

I3

Torque transmitted

By both friction surfaces      = 2x2  µ p [ D

D

/ 8x3 ] Kgf-cm

O3_

I3

=  /6 µ p [ D

D

] Kgf-cm -----2

O3_

I3

Comparing equations 1 and 2,

/2 ( Do

– Di

) µ p

R

=  /6 µ p [ D

D

]

2

2

m

O3_

I3

R

= 1 / 3 [[ D

D

/ Do

– Di

]

2

2

m

O3_

I3

Now substitute Value of R

in equation----- 1.

m

Torque transmitted

By both friction surfaces    =  /2  µ p

R

( Do

– Di

)

Kgf-cm

2

2

mech

m

=  /6  µ p

[ D

D

]

Kgf-cm

mech

O3_

I3

Torque capacity of clutch T  = /600  µ p

[ D

D

]

Kgf-m

mech

O3_

I3

Rated torque capacity of a clutch= T / R

F

Then Rated torque capacity   =  /600  µ p

[ D

D

] /  R

Kgf-m

mech

O3_

I3

F

DESIGN  ASPECTS OF CLUTCH

In passenger cars, pedal eff ort should be in the range of 10-12 kgf and

in commercial vehicles the range should be 20-24 kgf.

Let

E1 be energy required to compress the clutch for disengagement

E2 be energy required to overcome friction of clutch components

E3 be elastic deformation of clutch disengaging components

Then E2 + E3 = 0.6E1

Thus total energy required = E1+E2+E3= 1.6 E1

CLUTCH GRAB

Grab  is  the  sudden  jerky  motion  of  the  vehicle  when  clutch  pedal  is

released.

CLUTCH CLATTER

Clatter is the alternative movement of the clutch disc between flywheel

and pressure plate. (Or) A shaking or shuddering of the vehicle as the clutch

is operated.

CLUTCH DRAG

A  problem  in  which  the  clutch  disc  does  not come  to  a  complete  stop

after the clutch pedal is depressed.

CUSHION SPRINGS

The  clutch  clatter  is  avoided  by  providing  cushion  spring  between

friction facings. Cushioning device consists of waved cushion springs to which

the facings are riveted. These springs compress slightly as the clutch engages

producing a cushioning effect.

DAMPER SPRINGS

Torsional vibration damper hub is provided in steel disc to prevent the

torsional vibration of the engine from being transmitted through clutch which

would  result  in gear and  driveline noises.  Coil springs are  generally used to

provide torque build up as hub is rotated with respect to the clutch plate. The

pressure of the coil spring is designed to produce a counter torque as high as

the torque transmitted by the engine.

FRICTION MATERIALS

Mill board type

1.  Woven type- a) laminated b) solid woven

2.  Moulded or composition type

MOULDED TYPE

This type of lining is composed of asbestos fibers in their natural state

mixed with a bonding material and then moulded in dies under pressure and

at  elevated  temperature.  Metallic  wires  are  sometimes  included  only  to

increase  the  wear  qualities  and  to  eliminate  scoring  of  metal  faces  against

which the lining rubs.

CLUTCH COMPONENTS MATERIALS

Components  Material  Components  Material

Cover plate  Mild steel  Damper spring  Spring steel

Diaphragm spring  Spring steel  Clutch hub  Mild steel

Coil spring  Spring steel  Bolts to fasten flywheel and cover plate  Steel

Pressure plate  Cast iron  Rivets on cushion spring  Brass

Clutch disc  Mild steel  Retainer spring  Spring steel

Friction facing  Asbestos base  Damper spring retainer plate  Mild steel

Rivets on facing  Aluminum brass  Cushion spring  Mild steel

PROBLEMS ON CLUTCH D ESIGN

Torque transmitting capacity of clutch

According to Uniform pressure theory

Torque transmitted by clutch = T =    2 x   x W x n x ( r

³-r

³)     N-m

2

1

3                        ( r

²-r

²)

2

1

According to Uniform wear theory

Torque transmitted by clutch = T =    x W x n x  ( r

+r

)     N-m

2

1

2

C = pr = Constant =    ____W____

2 (r

-r

)

2

1

Where,

W = Axial load exerted by actuating spring in N

µ = coefficient of friction between the contact surf aces.

P = normal pressure in Pa

r

and r

= internal and external radii of contact surface in m

1

2

n = No. of contact surfaces

n = n

+ n

–1

1

2

n

and n

are no. of driving plates and no. of driven plates respectively

1

2

A motorcar engine develops 5.9 b.k  W  at 2100rpm. Find  the suitable  size

1.

of  clutch plate  having  friction  linings riveted  on both  sides, to transmit

the power, under the following conditions:

(i)  Intensity of pressure on the surface not to exceed 6.87x10  pa.

(ii)  Slip torque and losses due to wear etc. is35% of engine torque.

(iii)  Coefficient of friction on contact surface is 0.3.

(iv)  Inside diameter of the friction plate is 0.55 times the outside diameter.

T = P

x 60000  =  60000 x 5.9   =   26.84 N-m

w

2 N           2  x 2100

Taking account of the losses, the total torque is

T = 26.84 x 1.35  =  36.23 N-m

We, have

T = 2  µC (r

-r

)

22

12

36.23  = 3.14 x 0.3 x 6.87 x 10

x r

[(r

/0.55)

– r

] x 2

4

2

1

1

12

= 3.14 x 4.122x10

[(1/0.303) –1] r

4

13

=        36.23 x 0.303                =  1.22 m

r13

3

3.14 x 4.122 x 10

x 0.697              10

4

4

r

= 49.5 mm      r

= 90 mm

1

2

Hence,

Inside diameter   = 99 mm

Outside diameter = 180 mm

NECESSITY OF GEAR BOX IN AN AUTOMOBILE

The  gear  box  is  necessary  in  the  transmission  system  to

maintain  engine  speed at the  most  economical value  under  all  conditions  of

vehicle mo vement. An ideal  gear box would provide an  infinite range of  gear

ratios, so that the engine speed should be kept at or near that the maximum

power is developed what ever the speed of the vehicle.

FUNCTION OF A GEAR BOX

1.  Torque  ratio  between  the  engine  and wheels to  be  varied  for

rapid acceleration and for climbing gradients.

2.  It provides means of reversal of vehicle motion.

3.  Transmission  can  be  disconnected  from  engine  by  neutral

position of gear box.

TYPES OF GEAR BOX

PROGRESSIVE TYPE  GEAR BOX

Usually this gear boxes are used in motor cycles. In this gear boxes the

gears  pass through  the intervening  speeds while  shifting  from  one  speed  to

another. There is a neutral position between two positions. These gear boxes

are a combination of sliding and constant mesh gear boxes. The various gear

speeds are obtained by sliding the dog clutch or gear to the required position.

EPICYCLIC (OR) PLANETARY TYPE GEAR BOX

The  epicylic  or  planetary  type  transmission  uses  no  sliding  dogs  or

gears  to  engage  but different  gear  speeds  are obtained  by  merely tightening

brake-bands  on  the  gear  drums, which  simplify  gear  changing.  A  planetary

gear  set  consists  of  ring  gear  or  annular  wheel,  sun  gear  and  planet  gears

with carrier. In order to obtain  different speeds any one  of these  three units

can be held from rotation by means of brake bands.

SELECTIVE TYPE GEAR BOX

It  is  the  transmission  in  which  any  speed  may  be  selected  from  the

neutral  position.  In  this  type  of  transmission  neutral  position  has  to  be

obtained  before  selecting  any  forward  or  reverse  gear.  Some  selective  type

gear boxes are,

1.  Constant mesh gear box with positive dog clutch.

2.  Constant mesh gear box with synchromesh device.

3.  Sliding mesh gear box.

SLIDING MESH GEAR BOX

It is the simplest and oldest type of gear box.

1.  The clutch gear is rigidly fixed to the clutch shaft.

2.  The  clutch  gear  always  remains  connected  to  the  drive  gear  of

countershaft.

3.  The other lay shaft gears are also rigidly fixed with it.

4.  Two gears are mounted on the main shaft and can be sliding by shifter

yoke when shifter is operated.

5.  One  gear  is  second  speed  gear  and  the  other  is  the  first  and  reverse

speed gears. All gears used are spur gears.

6.  A reverse idler gear is mounted on another  shaft  and  always  remains

connected to reverse gear of counter shaft.

FIRST GEAR

By operating  gearshift  lever, the larger gear  on main  shaft is made to

slide  and mesh  with  first  gear  of  countershaft.  The  main  shaft  turns  in  the

same direction as clutch shaft in the ratio of 3:1.

SECOND GEAR

By  operating  gear  shaft  lever,  the  smaller  gear  on  the  main  shaft  is

made to slide and mesh with second gear of counter shaft. A gear reduction of

approximately 2:1 is obtained.

TOP GEAR

By  operating gearshift  lever,  the combined  second speed gear  and top

speed gear is forced axially against clutch shaft gear. External teeth on clutch

gear mesh with internal teeth on top gear and the gear ratio is 1:1.

REVERSE GEAR

By  operating  gearshift lever,  the  larger  gear of  main shaft is  meshed

with  reverse  idler  gear.  The  reverse  idler  gear  is  always  on  the  mesh  with

counter  shaft  reverse  gear.  Interposing  the  idler  gear, between  reverse  and

main shaft gear, the main shaft turns in a direction opposite to clutch shaft.

NEUTRAL GEAR

When  engine  is  running  and  the  clutch  is  engaged,  clutch  shaft  gear

drives the drive gear of the lay shaft and thus lay shaft also rotates. But the

main shaft remains stationary as no gears in main shaft are engaged with lay

shaft gears.

CONSTANT MESH GEARBOX

In this type of gearbox, all the  gears of the main shaft are in constant

mesh  with  corresponding  gears  of  the  countershaft.  The  gears  on  the  main

shaft  which  are bushed  are  free  to  rotate. The dog clutches are  provided  on

main shaft. The gears on the lay shaft are, however, fixed.

When  the  left  Dog  clutch  is  slid  to  the  left  by  means  of  the  selector

mechanism, its  teeth  are engaged  with  those  on  the  clutch  gear  and  we  get

the  direct  gear.  The  same  dog  clutch,  however,  when  slid  to  right  makes

contact with the second gear and second gear is obtained.

Similarly  movement  of  the  right  dog  clutch  to  the  left  results  in  low

gear and towards right in  reverse gear. Usually the helical gears are used in

constant mesh gearbox for smooth and noiseless operation.

SYNCHROMESH GEARBOX

This  type  of  gearbox  is  similar  to  the  constant  mesh  type  gearbox.

Instead of  using  dog  clutches  here  synchronizers are  used.  The modern cars

use helical gears and synchromesh devices in gearboxes, that synchronize the

rotation of gears that are about to be meshed.

SYNCHRONIZERS

This type of gearbox is similar to the constant mesh type in that all the

gears  on  the main  shaft  are in  constant mesh  with the  corresponding  gears

on the lay shaft. The gears  on the lay shaft are fixed to it while those on the

main  shaft  are free to rotate on the  same.  Its working is also  similar  to  the

constant mesh type, but in the f ormer there is one definite improvement over

the  latter.  This  is  the  provision  of  synchromesh  device  which  avoids  the

necessity of  double-declutching. The  parts  that ultimately  are to be engaged

are  first  brought  into  frictional  contact,  which  equalizes  their  speed,  after

which these may be engaged smoothly.

Figure shows the construction and working of a synchromesh gearbox.

In most of the cars, however, the synchromesh devices are not fitted to all the

gears as is shown in this figure. They are fitted only on the high gears and on

the  low  and  reverse  gears  ordinary  dog  clutches  are  only  provided.  This  is

done to reduce the cost.

In figure A is the engine is the engine  shaft, Gears B, C, D, E  are free

on  the  main  shaf t  and are  always in  mesh with corresponding  gears  on  the

lay shaft. Thus all the gears on main shaft as well as on lay shaft continue to

rotate so long as shaft A is rotating. Members F1 and F2 are free to slide  on

splines  on  the  main  shaft.  G1  and  G2  are  ring  shaped  members  having

internal teeth fit onto the external teeth members F1 and F2 respectively. K1

and K2 are dogteeth on B and D respectively and these also fit onto the teeth

of G1 and G2. S1 and S2 are the forks. T1 and T2 are the balls supported by

spring.  These  tend  to  prevent  the  sliding  of  members  G1  (G2)  on  F1  (F2).

However  when  the  force  applied  on  G1  (G2)  slides  over  F1  (F2).  These  are

usually  six  of  these  balls  symmetrically  placed  circumferentially  in  one

synchromesh  device.  M1,  M2,  N1,  N2,  P1,  P2,  R1,  R2  are  the  frictional

surfaces.

To  understand  the  working  of  this  gearbox,  consider  figure  which

shows in steps how  the  gears  are engaged.  For  direct gear,  member G1 and

hence member F1 (through spring- loaded balls) is slid towards left till cones

M1  and  M2  rub  and  friction  makes  their  speed  equal.  Further  pushing  the

member G1 to left causes it to overdrive the balls and get engaged with dogs

K1.  Now the drive  to  the main shaft is direct  from B  via  F1 and  the splines.

However, if  member  G1 is pushed  too quickly so  that  there  is  not sufficient

time  for  synchronization  of  speeds,  a  clash  may  result.  Likewise  defect will

arise in case springs supporting the balls T1 have become weak.

Similarly for second gear the members F1 and G1 are  slid to the right

so that finally the internal teeth on G1 are engaged with L1.  Then the  drive

to main shaft will be from B via U1, U2, C, F1 and splines. For first gear, G2

and  F2  are  moved towards left.  The  drive  will be from  B via  U1, U2,  D, F2

and splines  to  the main shaft. For  reverse  gear,  G2 and  F2  are slid towards

right. In this case the drive will be from B via U1, U2, U5, E, F2 and splines

to the main shaft.

A  synchro's  purpose  is  to  allow  the  collar  and  the  gear  to  make

frictional contact  before the dog teeth make contact.  This  lets the  collar and

the gear synchronizes their speeds  before the teeth need to engage,  like this:

The  cone  on  the  blue  gear  fits  into  the  cone-shaped  area  in  the  collar,  and

friction  between the cone and the  collar  synchronize the  collar  and the gear.

The  outer  portion  of  the collar  then  slides so  that  the dog  teeth  can  engage

the gear.

DETERMINATION OF GEAR RATIOS

From one point of view,  the ideal type  of transmission  is the  so  called

indefinitely  variable  gear,  in  which  torque  ratio  can  be  varied  continuously

within  wide  limits,  because  it  permits  of  operating  the  engine  at  all  times

under  optimum  conditions  with  respect  to  both  fuel  consumption  and  wear

and tear.  However in  an ordinary transmission  only  a  small number of  gear

ratios can be provided to cut down expenses and weight. The most desirable

number of gear changes depends in part on the use to which the transmission

is to be put, and each field of application must be considered separately.

The  most  desirable  number  of  gear  ratios  depends  on  the  difference

between  highest  and  lowest  gear  ratios.  The  larger  the  ratio  between

corresponding  gear  ratios,  the  more  difficult  it  is  to  make  the  change  from

one  gear  to  another,  it  must  be  done  by  either  shifting  gears  into  mesh

laterally or securing a gear to its shaft by means of a jaw clutch. A ratio of 2:1

is about the limit and is frequently used in trucks although a ratio of 1.5:1 is

considered better from a standpoint of ease shifting.

Formerly a ratio of 1:8 was used in passenger cars and high speed was

a  direct  drive  with  a  ratio  of  1:1,  the  intermediate  speed  a  reduction  gear

with a1:8 ratio and the low speed a reduction gear with a ratio of (1.8 x 1.8): 1

or  3.24:1.  When  gear  ratios  are  arranged  in  such  an  order  they  form  a

geometrical  series  which  offers  certain  advantages  from  the  standpoint  of

operation.  In most  automotive  transmission  the ratios of  the different  gears

come  fairly  close  to  forming  a  geometric  series.  A  slight  deviation  from  the

series is made at high speed end. There are certain limitations on the number

of gear tee th which can be provided, and it is therefore not always possible to

obtain an exact geometrical series of ratios, even if that should be desired.

GEAR RATIO CALCULATION FOR SMALL CARS

HIGH GEAR RATIO (TOP GEAR RATIO)

Power required to propel the vehicle   HP =  R

V / 270

t

t

R

= Ra

+ R

+ R

t

r

g

Where

V = vehicle speed in kmph

= transmission efficiency

t

R

= total resistance in N

t

In top gear R

= 0     R

=  R

+ R

g

t

a

r

Maximum speed   V = N R

/ 2.65 G

r

w

Where

N = Engine speed in rpm

R

= Wheel Radius

w

G = gear ratio in top gear 1:1

r = permanent reduction in the final drive.

LOW GEAR RATIO (FIRST GEAR RATIO)

Assume that gradient resistance is high.

R

= Ra

+ R

+ R

t

r

g

Tractive force available at the driving wheel

F

T

G

r / R

w =

e  t

w

T

= 4500 * P / 2   N

e

T

= Engine torque

e

From this G

can be calculated.

1

INTERMEDIATE GEAR RATIOS

To calculate intermediate gear ratios the decisions to be taken for

1.  Number of intermediate gear ratios

2.  Step  between  two  successive  gear  ratios.  It  should  not  exceed  1.5  for

small cars, 1.8 for truck, and 1.9 for tractor.

In first gear, the vehicle speed     V

= N

R

/ 2.65 G

r-------1

1

1

w

1

Gear ratio is in geometrical progression ratio

During gear shifting        V

= N

R

/ 2.65 G

r

1

2

w

2

= x (N

/ G

)   ------2

2

2

Where x =

R

/ 2.65

r = constant.

w

Equate 1 and 2         x (N

/ G

)

=  x (N

/ G

)

1

1

2

2

G

= ( N

/ N

) G

2

2

1

1

In second gear, the vehicle speed    V

= N

R

/ 2.65 G

r-------3

2

1

w

2

Gear ratio is in geometrical progression ratio

During gear shifting        V

= N

R

/ 2.65 G

r

2

2

w

3

=  x (N

/ G

)   ------4

2

3

Where x =

R

/ 2.65

r = constant.

w

Equate 1 and 2         x (N

/ G

)

=  x (N

/ G

)--------4

1

2

2

3

G

= ( N

/ N

) G

3

2

1

2

Substitute G

value in G

2

3

G

= ( N

/ N

)

G

2

3

2

1

2

Similarly

G

= ( N

/ N

)

G

3

4

2

1

1

Practically the gear shifting operation from top to next is frequent one.

Hence this shifting operation should be smoother. In  order to achieve the

easier operation the step between these two gears is reduced.

ADVANTAGES OF GEOMETRICAL SERIES

The  advantage  of  gear  ratios  following  a  geometrical  series  is

explained with  reference  to  figure.  The  figure  shown  applies to a four  speed

truck  transmission,  the  truck  being  so  geared  that  when  in  direct  drive  it

attains  a  speed  of  48  mph  with  the  engine  running  at  2800  rpm.  The  four

ratios in the transmission are 6.64, 3.53, 1.88 and 1.00.

The  vehicle  is accelerated to a speed  of 6 miles/hour in  first gear with

engine  speed  2400  rpm.  It  is  indicated  by  the  first  slope  line.  For  further

acceleration the  driver shifts to second  gear  which reduces the engine  speed

proportional  to  1.88:1  if  the  engine  is  directly  coupled  to  drive  wheels,  but

since  the  clutch  is  allowed  to  slip  for  some  time, The  vehicle  accelerates  in

second  gear  with  the  clutch  slipping,  and by the  time  the  drive  has  become

positive,  it  will  move  ahead  at  higher  speed.  It  is  indicated  by  the  dotted

lines, connecting the first gear and the second gear acceleration lines.

In second gear, the truck is allowed  to accelerate until  engine  reaches

2400 rpm.  Then  the gear  is shifted  to  third and again the  vehicle  is brought

up  to  a  speed  of  2400  rpm.  After  this  the  transmission  is  shifted  to  high,

which once more slows down and tries to achieve maximum speed. The entire

process  of  vehicle  acceleration  therefore  consists  of  engine  acceleration  and

deceleration  and  if  gear  ratios  are  in  geometric  order,  the  engine  can  be

accelerated through the same speed range in each gear.

It  is  advisable  not  to  accelerate  to  too  high  an  engine  speed,  as  high

speeds are injurious, and it is also advisable not to slow the engine down too

much, as at very low speeds it operates jerkily, which also is injurious. If the

engine  is  accelerated  through  the  same  speed  range  in  each  gear,  the

conditions would seem to be the best, except f or one fact-that the torque load

is greater in high gear than in  any of the lower ones, and the engine is more

likely to be rough in high gear if its speed is reduced too much.

This is  one of  the reasons  why it  is a general practice in  transmission

design to make the step between the highest and the next gear smaller than

the step between any other two gears. Another reason is that  the shift from

one  gear  to another is  easier  to  make  the  smaller the  step  between the  two

gear ratios, and in traffic driving the change from high gear into the next and

back again had to be made quite frequently than any other.

PERFORMANCE CHARACTERISTICS

The  above  graph  gives  the  relation  between  car  speed  and  total

resistance, tractive effort at the different gear ratios and different gradients.

From  the  figure,  the  curves  A  to  F  are  curves  of  total  resistance  for  a  road

with  uniform  surface  but  of  varying  gradient,  curve  A  being  level  and  the

curve  F  the  steepest  gradient.  Curves  RS,  TU,  VW  are  curves  of  tractive

effort for three different types of gear ratios.

Suppose the vehicle is traveling on the level at a speed represented by

OX.  Then  resistance  to  be  overcome  is  XY  and  XZ  is  the  tractive  effort

available.  The  tractive  effort  available  is  therefore  greater  than  the

resistance to be overcome and the excess tractive effort YZ will go to increase

the speed of the vehicle.

Thus  during acceleration,  the resistance  increases  and  extra effort  for

acceleration reduces. When the speed is OM, the total tractive effort is equal

to total resistance. Thus speed cannot be increased further.

If the vehicle now comes to a gradient to which the curve B applies. At

the  speed  OM  on  gradient  B,  the  resistance  is  MN.  But  tractive  effort

available  is only MH. Thus excessive  resistance MN will reduce speed of the

vehicle to the point I where tractive effort is equal to the resistance.

Now suppose the gradient  becomes steeper and steeper, so we pass in

succession from curve B to C and so on. Then speed maintained lowers down

to  the  points  J,  K  etc.  It  is  seen  that  we  can  traverse  the  gradient  at  any

speed, since tractive effort at III gear lies everywhere below resistance curve.

In  such  cases,  the  gear  has  to  be  shifted  to  second  and  the  speed  can  be

maintained at the point G.

GEAR BOX DESIGN

Power required to for propelling the vehicle (P

)

v

P

=   RV     kw

v

3600

Where

V = speed of the vehicle in km / hr

= transmission or drive line ef ficiency

t

R = total resistance in N

R

= air resistance in N

a

R

= rolling resistance in N

r

R

= grade resistance in N

g

R = (R

+R

) when vehicle moves along a level road.

a

r

R = (R

+R

+R

) when vehicle moves up a gradient.

a

r

g

Engine power required (P

)

req

P

P

=    RV     KW

req  =

v

3600

t

t

Air resistance

R

= K

AV

2

a

a

Where

A = projected frontal area, m

2

V = speed of the vehicle, Km/hr

K

= coefficient of air resistance

a

= 0.023 for best streamlined cars

= 0.031 for average cars

=   0.045 for trucks and Lorries

Rolling resistance

R

= KW

r

W = total weight of the vehicle, N

K = constant or rolling resistance and depends on the nature of road surface

and types of tyres

=  0.0059 for good surface

=  0.18 for loose sand roads

=  0.015, a representative value

Grade resistance

R

= Wsin

g

W = total weight of the vehicle, N

= inclination of the slope of the horizontal.

Traction and tractive effort

The  force  available  at  the  contact  between  the  rear  wheel  tyres  and

road  is  known  as  tractive  effort.  The  ability  of  the  rear  wheels  to  transmit

this effort without slipping is known as traction. Hence usable tractive effort

will never exceed traction.

Engine torque, T

= 60000P

N-m

e

e

2pN

Torque at rear wheels,

T

= (g.r.*a.r.)  T

G

T

w

e =

t

e

Tractive effort, F = T

= T

G

N

W

e

t

r          r

P

= engine b.p., KW

e

T

= mean engine torque in N-m

E

= overall transmission efficiency

t

g.r. = gear box gear ratio

a.r. = back axle ratio

G   = overall gear ratio = (g.r. * a.r.)

R = radius of tyre in metre

N = r.p.m. of crank shaft

When  the tractive  effort F>R, the  total  resistance  on level  road,  the surplus

tractive effort is utilized for acceleration, hill climbing and draw-bar pull.

Relation between engine revolutions, N and Vehicle speed, V

N/V ratio depends upon the overall gear ratio. A vehicle having four different

gears will have four different values of N/V ratio. V is km/hour and r is in

metre.

2 rN    = 1000V

G          60

N = 1000 G    = 2.65 G

V     2 r x 60             r

PROBLEMS ON GEAR BOX

1.  Find  out  the  axial  force  required  to  synchronize  the  speeds.    Given

coefficient  of  friction  =  0.04,  cone  angle  is  10  degree,  angular

acceleration is 50 rad/sec², moment of inertia 254 kg cm² and the mean

radius of the cone surface 4.13 cm.

Torque = Moment of Inertia in kg-cm² x Angular Acceleration in rad/sec²

Acceleration due to gravity in cm/sec²

T = I x a

g

T = 254 x 50 = 12.95 kg-cm

981

Torque = Mean Radius of cone x Axial Force in N x Coefficient of friction

Cone Angle

T = r x W x

Sin

12.95 = 4.13 x W x 0.04

Sin 10°

W = 13.31 kg

Axial force required W = 130.64 N

2.  In  a  gear  box  the  clutch  shaft  pinion  has  14  teeth  and  low  gear  main

shaft  pinion  32  teeth.  The  corresponding  lay  shaft  pinions  have  36  teeth

and 18 teeth. The axle ratio is 3.7:1 and effective radius of the rear type is

35.5  cm.  calculate  the  car  speed  in  the  above  arrangement  at  an  engine

speed of 2500rpm.

Determination of gear ratio:

CLUTCH SHAFT GEAR

MAIN SHAFT GEAR

LAY SHAFT GEAR A LAY SHAFT GEAR B

Gear Ratio =   Speed of the clutch shaft x Speed of the Lay shaft

Speed of the Lay shaft x Speed of the main shaft

Gear Ratio =

No. of teeth on the lay shaft Gear A x No. of teeth on the main shaft Gear A

No. of teeth on the clutch shaft Gear A x No. of teeth on the lay shaft Gear B

= 36 x 32 = 4.57:1

14 x 18

The rear axle ratio is 3.7:1

Hence the overall gear ratio,

G= 4.57 x 3.7:1 = 16.92:1

Speed of the car, V = 2   N r = 2  x 0.355 x 60  m/min

G         16.92

= 2  x 2500 x 0.355 x 60 km/hr

16.92 x 1000

= 19.8 km /hr

3.  A  truck  has  a  gross  vehicle  weight  of  89026  N.  engine  displacement  is

10m

,  power  77.3kW  at  governed  speed,  of  2400  r.p.m.  maximum  torque,

3

345.8 Nm at 1400r.p.m. Rear axle ratio 6.166: 1. fourth speed reduction ratio

in  transmission,1.605  :1,  drive  line  losses  amount  to  10.7kW  at  2400r.p.m

and  6.3  kW  at  1400  r.p.m.  tyre  size  0.4572  m  x  1.016  m  (effective  wheel

diameter 0.950 m),f rontal area of  truck  6.95mcalculate the  grades  which the

vehicle can climb in fourth gear in still air conditions.

(i) At governed engine speed; and

(ii) At speed of maximum torque, in the equation

R = KW +Ka A V²

Ka= 0.0462 where V in km/hr

Overall gear ratio   G= 6.166x1.605:1=9.9:1

(a) At governed speed,

We have, V =2  Nr

G

=2  x 2400 x .575   = 724 m/min

9.9

= 724x60  = 43.44 km/hr

1000

Total  resistance  in  climbing  the  grade,  inclination     to  the  horizontal  at

the above speed

R=KW + K

AV

+ W sin

2

a

= 0.014 x 89026 + 0 .0462 x 6.95 x (43.44)

+ W sin

2

= 1246.4 + 606 + 89026 sin

Power available at the road wheels = 77.3-10.7 = 66.6 KW

Tractive effort, F=66.6x 3600  = 5519.3 N

43.44

Since the car is moving at uniform speed, then

5519.3 = 1852.4 + 89026 sin

Therefore sin  =  3666.9   =    1

89026      24.3

As sin   is very small;  sin - tan  .

Hence grade is 1 in 24.3.

(b) At speed of maximum torque

V= 2  x 1400 x 0.475  =  422 m/min = 25.32 km/hr

9.9

Total resistance in the grade when going up at 25.32 km/hr

R = 0.014 x 89026 + 0.0462 x6.95 x 25.32

+ 89026 sin

2

= 1246.4 + 205.9 + 89026 sin

= 1452.3 + 89026 sin

Power available on the wheels = 2 NT  - 6.3

60000

= 2  x 1400 x 345.8 – 6.3

60000

= 50.7 – 6.3 = 44.4 KW

Tractive effort, F= 44.4 x 3600  = 6312.8N

25.32

As the car is moving with uniform speed, then

F=R

Or   6312.8 = 1452.3 + 89026 sin

Therefore, sin  = 4860.5  =    1

89026     18.3

Since sin - tan  for small value of  , grade is 1 in 18.3.

7.  4. The coefficient of rolling resistance for a truck weighing 62293.5 N is

0.018  and  the  coefficient  of  air  resistance  is  0.0276  in  the  formula

R=KW+KaAV²,  N,  where  A  is  m²  of  frontal  area  and  V  the  speed  in  km/hr.

the transmission efficiency in  top gear of 6.2:1  is 90% and that in the second

gear  of  15:1  is  88%.  The  frontal  area  is  5.574  m².  If  the  truck  has  to  have

maximum speed of88km/hr. in top gear calculate.

8.    (i) the engine b.p required;

9.    (ii)  the  engine  speed  if  the  driving  wheels  have  an  effective

diameter of    0.8125m;

(iii) The maximum grade the truck can negotiate at the above engine

speed in second gear

(i)  R = 0.018 W + 0.0276 AV

2

= 0.018 x 62293.5 + 0.0276 x 50574 (88)

2

= 1121.3 + 1191.4 = 2312.7 N

Engine b.p = RV     =      2312.7    x      88

1000

1000 x 0.9         3.6

t

= 62.8 b.p.

(ii)    V = 2 rN  m/min

G

N  = VG = 88 x 1000     x               6.2

2 r        60         2 x 3.14 x 0.40625

=           88 x1000 x 6.2

60 x 2 x 3.14 x 0.40625

= 3564 rpm

(iii)In second gear

V = 88 x 6.2 = 36.4 km/hr = 36.4 m/s

15                                     3.6

R = 0.018 x 62293.5 + 0.0276 x 5.574 x 36.4

2

= 1121.3 + 203.8 = 1325.1 N

If it can climb the maximum grade of 1 in X, then

R = [1325.1 + (622293.5/x)]

We have

F = b.p x

x1000

t

V

= 62.8 x 0.8 x1000 x   3.6 = 4968.8 N

36.4

Hence,

1325.1 + 622293.5 = 4968.8

X

Therefore,

X = 62293.5 = 17.1

3643.7

Hence maximum grade is 1 in 17.1

(iv)Maximum drawbar pulls on level road

= Tractive effort available – Tractive effort for resistance on level road

= 4968.8 – 1325.1 = 3643.7 N

UNIT II

HYDRODYNAMIC DRIVE

FLUID COUPLING

Fluid coupling is a device which is used to transmit torque from engine

to gear box with fluid as working medium. The purpose of fluid coupling is to

act as flexible power transmitting coupling.

CONSTRUCTION DETAILS AND PRINCIPLE OF OPERATION

The function of the FC is to act as an automatic clutch between engine

and gearbox. It allows the engine to idle when the car is stationary but takes

up  the  drive  smoothly  and  progressively  when  the  driver  speeds  up  the

engine by depressing the accelerator pedal.

T I

T I

There  are  two  main  rotating  parts;  an  impeller  driven  by  the  engine

and  a  turbine  which  drives  gearbox.  Each  is  bowl  shaped  and  contains  a

number of  partitions called vanes. The two bowls are placed face to face in a

casing filled  with oil, and they are  separated by  a small clearance so that no

rubbing contact between them.

The  basic  form  of  the  fluid  drive  known  as  fluid  flywheel  or  fluid

coupling is used in place of friction clutch in cars with pre-selector gearboxes.

It  generally  consists  of  an  impeller  and  a  turbine  with  oil  continuously

circulated  between  the  two  when  engine  is  running.  When  the  engine  is

idling, the oil is flung from the impeller by centrifugal force. Directed forward

by the vanes, it enters turbine which remains stationary because the force of

oil is not yet sufficient to turn it.

When  the  driver  depresses  the  accelerator  pedal,  impeller  speed

increases  and  turning  ef fect  derived  from  fast  moving  oil  becomes  great

enough  to  overcome the  resistance  of  the  turbine,  which  begins  to  rotate so

setting  the car in  motion.  After giving  up the  energy  to  turbine,  oil  reenters

the  impeller  and  is  circulated  back  to  the  impeller  again.  If  the  speed  of

engine continues to increase,  the difference between the  rotational  speeds of

impeller  and  turbine  gradually  diminishes  until  the  slip  between  then  is

reduced  to  as  little  as  2%.  The  limitations  of  FC  is  that  torque  applied  to

turbine can never be greater that that delivered by impeller.

IDLING

The  driving part  of FC is attached  to the  engine and  faces  the driven

part from which it  is separated by small clearances. At idling speed, there is

insufficient centrifugal force for the oil to turn turbine and to move the car.

LOW TO MEDIUM REVOLUTIONS

As  the engine speeds  up,  centrifugal  force pushes oil into turbine and

some turning effort is  transmitted. But there is still a large  degree of  slip in

the unit. The output shaft is thus rotating more slowly than input shaft.

MEDIUM TO HIGH REVOLUTIONS

Once  the  engine  reaches  a  preset  speed,  the  oil  forces  is  sufficient  to

transmit  full  power.  This  gives  in  effect  a  direct  drive  with  output  shaft

rotating at about 98%of speed of input shaft.

ADVANTAGES OF FLUID COUPLING

1.  It  provides  acceleration  pedal  control  to  effect  automatic

disengagement of drive to gearbox at a predetermined speed.

2.  Vibrations  from  engine  side  are  not  transmitted  to  wheels  and

similarly shock loads from transmission side will not be transmitted to

engine.

3.  The engine will not stall if it is overloaded.

4.  No wear on moving parts and no adjustments to be made.

5.  No  jerk on transmission when  gear engages.  It  damps  all  shocks  and

strains incident with connecting a revolving engine to transmission.

6.  Vehicle  can  be stopped  in  gear  and  move  off  by  pre ssing  acceleration

only.

7.  There  is  no  direct  firm  connection  between  engines  and  wheels.  So

when engine is overloaded, it will not stop. But it results in slip within

coupling.

8.  Unlike  friction  clutch,  slip  within  coupling  does  not  cause  damage

within working components.

9.  In case of  FC, engine is not f orced to operate at very low speeds when it

is overloaded.

10. No wear is experienced on impeller or turbine blades.

TORQUE CAPACITY OF FLUID COUPLING

B

C

X

Y

R

A D

When slip is below 3%

The change is KE depends on,

1.  weight of fluid particles

2.  speed of impeller

3.  outer radius of coupling

i.e., change in KE    Proportional to W

Proportional to N

2

Proportional to R

2

Centrifugal force acting on impeller F

is proportional to N

2

1

Centrifugal force acting in turbine F

is proportional to n

2

2

When slip is constant,

n is proportional to N

i.e., F

is proportional to N

2

2

Resultant centrif ugal force F

-F

is proportional to N

,

2

1

2

But resistance to flow = F

-F

1

2

i.e., Resistance to flow is proportional to v

.

f2

N

is proportional to v

2

f2

Therefore, N is proportional to v

f

Number of flow circuits per unit time is proportional to v

f

Is also proportional to N

Power transferred =Energy per cycle x Number of cycles per unit time.

Energy per cycle is proportional to N

and W

2

Number of cycles per unit time is proportional to N and R

2

Case 1

Power transferred is proportional to N

and N

2

Power transferred is proportional to N

3

Torque transmitted = P/N,

i.e., T is proportional to N

2

Case 2

Power transferred is proportional to W x R

2

Wt of particle = volume x density i.e., W is proportional to D

3

Power transferred per cycle is proportional to D

x D

3

2

Total power transferred in a number of cycles is proportional to D

x N

5

Torque transmitted is proportional to D

5

From (1) and (2); T is proportional to N

and D

2

5

Thus, T = CN

D

2

5

Where, N= Impeller speed in hundreds of rpm

D= Outer diameter of coupling in m

C= coupling constant = 5.25

When Slip is upto10%

K.E. = ½ x W/g (2x3.14xN)(R

-r

)

2

2

Power transferred = Energy per cycle x Number of cycles per unit time

P is proportional to WN

(R

-r

) N

2

2

2

P=f(T,N) <=WN

(R

-r

)N

2

2

2

i.e., Torque T is proportional to WN

(R

-r

)

2

2

2

Up to 10% of slip,

Torque is directly proportional to slip

i.e., T is proportional to S

Therefore, T is proportional to SWN

(R

-r

)

2

2

2

Torque capacity T = C

SWN

(R

-r

) Kgf-m

2

2

2

1

Where, c1= 0.241 and S is in decimal.

If slip is 10%, then S= 0.1

R = (0.5(R

+R

))

m

1/2

12

22

r = (0.5(r

+r

))

m

1/2

12

22

DISADVANTAGE OF FULID COUPLING

Even  whe n the  engine  is  idling, runner shaft rotates i.e., some torque

is  transmitted  during  the engine  is  in idling condition. Due  to  this  the  gear

shifting  is  some  what  difficult  and  the  vehicle  will  tend  to  move  when  it  is

parked in gear.

DRAG TORQUE

The torque transmitted when the engine is in idling condition is known

as drag torque. Even when %slip is 100% there is a drag on GB shafts, which

renders gear changing with ordinary type of gearbox very difficult and vehicle

will tend to move when it is parked.

To reduce the drag torque, following methods are used,

1) Using anti drag torque baffle.

2) Using fluid reservoir.

3) Using combination of both.

4) Fluid coupling is used on combination with epicyclic gear box.

5) Fluid coupling with conventional synchromesh gearbox

ANTI-DRAG BAFFLE

It is a circular plate secured to either the impeller or the runner at the

inner circumference of  the torus,  and projecting  into  latter,  thus obstructing

the path of fluid flow. At normal operating speeds the liquid is carried toward

the circumference of coupling by centrifugal force, and it is found that under

these conditions the baffle does not affect circulation.

Under  idling  and  starting  conditions,  however,  the  velocity  of  the

runner  is  low  and  the  liquid  then  is  forced  by  the  centrifugal  force  of  the

vertex motion, so that its flow is greatly affected by the plate. As the speed of

the  runner  increases, the  centrifugal force  due to  runner  rotation  increases,

while  that  due  to  vertex  motion  decreases,  and  the  effect  of  baffle  then

gradually vanishes or reduced.

FLUID RESERVOIR

At  high  speeds,  when  the  liquid  is  forced  toward  the  other

circumference of  the  coupling by centrifugal  force, the  fluid coupling  will be

completely  filled  with  oil  and  the  fluid  coupling  will  transmit  maximum

possible torque in the reservoir.

The  chief  purpose  of  the  reservoir  is  to  reduce  the  drag  while  the

engine is idling, by partly empty in the torus by returning the oil to the torus

automatically with an increases in speed. It ensures allow slip and relatively

high efficiency of  the coupling at crossing speeds. Here  we can  safely e nsure

100%  filling  of  coupling.  Hence  the  maximum  torque  and  efficiency  is

increased.  But  the  fluid  reservoir  increases  the  overall  axial  length  of

coupling.

COMBINING ANTI-DRAG BAFFLE AND RESERVOIR

Using  both  the  anti-drag baffle  and  the  reservoir  in  the  same vehicle

we can reduce the drag torque by about 85 to 90%.

FLUID COUPLING WITH EPICYCLIC GEARBOX

The  fluid  flywheel  is  generally  used  in  combination  with  epicyclic

gearboxes which eliminates the drag torque.

FLUID  COUPLING  WITH  CONVENTIONAL  SYNCHROMESH

GEARBOXES

Auxiliary  clutches  are  used  during  gear  shift  operation.  This  type  of

transmission was used in Dodge fluid drive in 1950.

CHARACTERISTICS OF THE FLUID COUPLING

The  characteristic  which  is  of  chief  importance  is  the  way  in  which

percentage slip  varies with speed  of  rotation. The  percentage slip is defined

as  the quantity ((N-n)/N)*100 and is a measure of  the difference  in speed  of

two rotors. If ‘n’ were equal to ‘N’, then % slip would be zero and  if n=0 then

% slip would be 100.

When percentage slip is plotted against engine speed (N), the resulting

graph is the form as shown. At any speed less than about 600 rpm (this speed

can be made to have any desired value by suitably modifying the design), the

%  slip  is  100,  i.e.,  the  GB  shaft  is  stationary  and  we  have  equivalent  of

completely disengaged clutch.

100

80

60

40

20

0

500 1000 1500 2000 2500 3000

IMPELLER SPEED (rpm)

As  the  engine  speed  increases  from  600  to  1000  rpm,  the  % slip  falls

rapidly to about 12%. This corresponds to the period of actual engagement of

an ordinary clutch, the speed of GB shaft being rapidly brought up to roughly

the same value as engine speed. From 1000 rpm up to maximum speed, the %

slip  decreases  comparatively  slowly  from  12  down  to  possibly  as  little  as  2.

The  %  slip  at  any  engine  speed  depends  however  on  the  torque  being

transmitted.  The  curve  being  based  on  assumption  that  engine  exerts  full

torque  at  every  speed. If  the  engine  torque is reduced  below  the full  torque

(open throttle) value, the % slip will be reduced.

Thus % slip may be less than 1%. The chain dotted curve indicates the

variation of  %  slip  with  the speed f or  such  condition,  i.e.,  level road  and  no

head wind. Whatever  the value of  % slip,  however it represents a direct loss

of  energy  and  thus an  increase  in  fuel  consumption.  Thus,  it  is  an  abuse  of

fluid flywheel to allow the  engine speed  to fall  to  region between 100  to 600

rpm,  full  throttle  when  %slip  becomes  ordinary  clutch  which  also  increases

fuel  consumption,  the  difference  being  that  whereas  an  ordinary  friction

clutch  would  be  damaged  by  prolonged  slipping  but  FC  will  not  suffer  any

damage although it may become so hot as to burn ones hand if he touches it.

100

98%

80

60

40

20

0

0.1 0.2 0.3 0.4 0.5 0.6 0.7 0.8 0.9 1.0

SPEED RATIO

Figure shows that when speed ratio (n / N) is 0.9, the efficiency is maximum.

12

100

10

80

8

60

6

40

4

20

2

Full Load

0

0

10 20 30 40 50 60 70 80 90 100

SLIP - PER CENT

Figure shows Up to 10% of slip the torque is directly proportional to % slip.

PROBLEM ON FLUID COUPLING

1.  A  petrol  engine  develops  10  N-m  torque  at  maximum  BHP  speed  of

4000rpm. Determine the diameter of the impeller required to transmit

the torque for a slip of 3%.

Torque transmitting capacity of the fluid coupling with in 3% slip

T = C D

N

5

2

Where

C = A coefficient = 5.25

D = Diameter of impeller in m

N = Maximum speed of the impeller in hundreds of rpm.

T = 10 N-m = 5.25 x D

x 40

5

2

The diameter of the impeller D = 0.26 m

TORQUE CONVERTER

BASIC PRINCIPLE OF TO RQUE CONVERTER

On  automatic  transmissions,  the torque  converter  takes  the  place  of

the clutch found on standard shift vehicles.  It is there to allow the engine to

continue  running when  the  vehicle  comes  to  a  stop.   The principle behind  a

torque converter is like taking a fan that is plugged into the wall and blowing

air  into  another  fan  which  is  unplugged.   If  you  grab  the  blade  on  the

unplugged fan, you are able to hold it from turning but as soon as you let go,

it will begin to speed up until it comes close to the speed of the powered fan.

The difference with a torque converter is that instead of using air, it uses  oil

or transmission fluid, to be more precise.

TORQUE CONVERTER

Most cars with automatic transmission use a form of fluid drive known

as toque converter as the name implies, it converts the torque or tuning effort

of engine into higher torque needed by cars at low road speed. An increase in

torque  has  same  effect  as  changing  to  a  lower  gear;  so  a  TC  is  also  a  gear

reducer, acting like an extra set of gears before engine drive reaches gear box.

Like  fluid  flywheel,  TC  has  an  engine  driven  impeller  and  a  turbine

connected  to GB  input  shaft.  It  is  also able  to  deliver  a  higher  torque  than

that engine produces, because it is also able to deliver a higher torque and a

small  vane  wheel  known  as  reactor  (stator).  A  one  way  clutch  (ORC)  lock

reactor to gear box casing at lower engine speed.

In  a f luid  flywheel, oil returning  from turbine  tends to curb the  speed

of  impeller.  But  in  TC,  the vanes  of  locked  reactor  direct  oil  along  a  torque

favorable path  back  to  the centre of impeller  enabling it  to  give  extra thrust

to turbine blades.

At  pull  away  speeds,  Torque  Converter double  the  effort produced  by

engine. As engine picks up speed, this 2:1 increase in torque is reduced until

at cruising speed, there is no torque increase at all. The reactor is spun round

by oil at some rate as turbine. TC now acts like a fluid flywheel with reactor

‘free wheeling’ and having no torque increasing effort. Neither FC nor TC can

be epicycle transmission which aloe gear changing without disconnecting.

An  alternative  used  on  few  models,  is  to  provide  a  friction  clutch  in

addition  to  TC.  This  enables  a  synchromesh  gear  box to  be  used,  as  friction

clutch disconnects engine when gears are being changed.

CONVERTER COUPLING

The  converter  coupling  is  a  next  type  of  fluid  drive  to  consider.  This

type represents an attempt to combine the best part of converter performance

with  those  of  Fluid  Coupling.  Most  forms  of  converter  can  be  employed  as

coupling by means of small changes to the reactors.

The  converter  is  made  to  operate  as  a  coupling  by  releasing  the

reactors from external constraint at the time when the applied torque on this

member reverses direction. The reactor then rotates slowly so as to give least

resistance to the fluid flow. As a result, any torque applied to the pump alters

flow  conditions  in  a  way  that  induces  an  equal  torque  on  turbine  member.

Various  methods  of  controlling  the  reactor  have  been  utilized  but  most

convenient is the use of “f ree wheel” or “over running clutch” unit into reactor

so  that  it  is  free  to  rotate  in  some  direction  as  the  turbine  but  is  locked

against rotation in opposite direction.

Conditions  of  equilibrium,  ensures  that  torque  on  reactor  changes

direction when o/p torque has fallen to value of i/p, so that introduction of free

wheel  unit  provides  an  automatic  method  of  changing  fro m  converter  to

coupling  operation  at  correct  time.  This  change  over  point  is  normally

referred to as  “coupling  point”.  The resultant characteristics  is shown where

it is seen that best parts of converter and coupling efficiency curves have been

successfully combined.

5

100

CONVERTER

COUPLING

OPERATION

OPERATION

4

80

EFFICIENCY

3

60

2

40

1

20

CONSTANT INPUT TORQUE

0

0 0.2 0.4 0.6 0.8 0

1.0

OUTPUT

INPUT SPEED RATIO

It is noted that there is a slip in efficiency curve around coupling point

and effort to remove this  efficiency resulted  in some  interesting  innovations.

One  very  simple  improvement  involves  a  change  in  design  point  which  is

shifted  to  a  higher  speed  ratio,  when  it  will  be  seen  that  a  much  improved

efficiency  curve  is  obtained  for  the  higher  speed  ratio  at  the  expense  of

performance  at  lower  speed  ratio.  More  important,  however  is  the  rather

serious reduction  in torque  conversion which detracts  from the usefulness of

design if larger o/p torque ratios  are required. It  is fair  to  say, however  that

several American automobiles manufacturers appears to be concentrating on

this  type  of  converter-coupling,  used  in  conjunction  with  a  number  of  gear

ratios to amplify o/p torque.   One  feature  of  converter  coupling  which  is

not relived  by graphs plotted  to a speed ratio base  is the fact that transition

from  converter  to  coupling  after  reaching  the  coupling point  is  a  drawn  out

process which usually to be accelerated by increased input speed.

The reason for this sluggish coupling operation is that the curved blade

which  is required, in  turbine for converter operation is  not so suitable when

operating as a coupling. Moreover, the free-wheeling reactor introduces some

additional  friction in  fluid  circuit so that it  is very  difficult to obtain  a  curve

on  a  basis  of  turbine  o/p  speed  revolves  more  accurately  the  most  of  the

transition  from converter to  coupling  and performance  of converter coupling

as  been  redrawn  to  new  abscissa.  That  graph  illustrates  conditions  which

apply for full throttle acceleration. Normal occurring conditions where engine

runs at  reduced o/p torque  will  take  place at  or  near  coupling point.  At  this

point i/p  and  o/p  torque are equal but o/p speed  will be about  10%  less than

i/p speed, depending on converter design.

MULTISTAGE TORQUE CONVERTERS

For  the  highest  torque  ratios,  it  is  necessary  to  employ  multi-stage

converter. The M.S  converter  is  one  in which, the  circulating fluid  impinges

two or more turbine members separated by reactors. First stage of conversion

is  reached  when  the  fuel  has  traveled  through  the  impeller,  turbine  and

reactors and extra stages are sometimes  added to obtain a particular type of

performance.

The provision of an additional turbine is referred to as an extra stage

and  thus  conforms  to  steam  turbine  practice.  It  is  necessary  to  emphasize

that  additional  turbine  member  must  be  separated  by  a  reactor  from  a

previous  turbine  to  create  an  extra  stage,  and  should  not  be  confuse  with

practice of dividing the reactor  member for  instance into several parts, so as

to carry out operation of reactor in a number of phases.

The  reason  for  using  an  increased  number  of  stages  is  usually  to

increase torque conversion ratio but certain other advantages are obtainable.

A multistage converter having a turbine immediately preceding impeller has

advantage  that  as  the  vehicle  accelerates,  fluid  can  be  delivered  at  greater

velocity  head to turbine  which is enabled  to  rotate  at faster speed. This fact

extends  useful  range  of  converter  and  increases  it  power  rating.  The

increased  number  of  stages  may  increase f luid  friction  on  account  of  longer

circulation path, and efficiency of multistage converter tends to fall of rather

sharply  and  racing  usually  occurs  at  lower  speed  ratios  than  for  a  single-

stage converter.

5

100

4

80

EFFICIENCY

3

60

2

40

1

20

CONSTANT INPUT TORQUE

0

0

0

0.2

0.4

0.6

0.8

1.0

OUTPUT

SPEED RATIO

INPUT

Thus,  although  increased  torque  ratios  are  obtained  with  multistage

converter, it is noticed that all the forms of converter discussed so for exhibit

a similar o/p characteristic which is roughly parabolic in shape. Variations in

blade design  or  number  of stages  has  the effect  of moving the  peak of  curve

towards low ratio (stall) end of o/p speed  range or  towards  the higher  ratios

(racing).consequently  a  typical  Multi  Stage  converter  will  develop  an  o/p

torque  equal  to  about  2  ½  times  the  value  of  i/p  torque  at  its  maximum

efficiency  point.  But  as  the  turbine  accelerates,  the    falls  rapidly  and  o/p

torque soon falls to zero. This type of converters thus would give a good initial

acceleration of vehicle from rest but would be inefficient for a normal cruising

which  is  mainly  carried  out  at  unity  torque  ratio  (direct  drive).  For  this

reason, most MS or high torque ratio converters are used in conjunction with

a friction clutch are some other way of obtaining an efficient direct drive.

POLY PHASE CONVERTER-COUPLING

The next type of fluid drive represents an attempt to combine the best

operating characteristics of two or more different designs of converters into a

single  converter.  These  ideas  are  usually  incorporated  into  converter

couplings, but it is converter operation it takes place in several phases.

A  poly  phase  converter  coupling  is a  variation  of  a  normal  3-element

machine in which at least one  of the 3 basic members is divided into further

elements.  The  reactor  has  to  deal  with  fluid  flow  from  widely  changing

entrance direction and this member can be divided into a number of elements

which  adjusts  them  selves  to  the  changing  flow.  The  practice  of  dividing  a

rotating member into several elements is widely used at the present time and

it is usual to have 2&3 phases, each of which is represented by a bladed ring

element  which  is  also  rotate  freely  when  the  fluid  flow  has  changed  the

direction by a given amount. In this way, the elements of reactor enables the

operation  of  redirecting  the  flow  to  be  carried  out  in  a  number  of  distinct

phases, giving rise to the use of the term poly phase converter, or poly phase

converter coupling.

5

100

EFFICIENCY

3

4

80

1 2

3

60

2

40

1

20

CONSTANT INPUT TORQUE

0

0

0 0.2 0.4 0.6 0.8

1.0

OUTPUT

INPUT SPEED RATIO

This  method  is  not  confined  to  reaction  member,  and  impeller  or

turbine member may also  be  divided  into  a  number of  these  elements which

may  rotate  at  different  speed  by  the  introduction  of  free-wheel  units.  Such

free-wheeling  blade  elements  detach  themselves  from  parent  member  and

rotate  at  speeds  that  least resistance to  fluid  flow  occurs.  At  this  point,  the

detached  members  can  be  considered  as  turbines  at  raising  speed.  From

figure,  it  is  seen  that  efficiency  curve  combines  the  most  useful  parts  of

curves  of  three  different  converter  designs  as  the  fluid  drive  effects  a  three

phase  transition  from  converter  to  coupling.  Each    peak  is  related  to  a

particular  design  point  which  is  referred  to  as  one  of  the  three  separate

phases  of  particular  design.  The  poly  phase  converter  coupling  represents

modern  practice in which  entrance  losses are  almost completely removed  for

a useful range of speed ratios. There still remains a need to extend this useful

range  of  ratio  and  most  transmission  use  and  auxiliary  gear  box  to  give

increased  o/p  torque  for  improved  acceleration  and  for  climbing  steeped

gradient.

Although  there are a few transmission which include a certain features

not  covered  by  foregoing  5  basic  types,  all  known  design  can  be  properly

classified into one of three categories.

CHARACTERISTICS OF TORQUE CONVERTER

The  graph  (a)   shows  the  manner  in  which  torque-increases  and

efficiency  vary  when  rotor  speed  varies  from  zero  to  maximum  value  (2700

rpm) the impeller speed  being constant at  300 rpm. When the rotor speed  is

zero  (because  the  resistance  opposing  its  motion  is  large  enough  to  hold  it

fixed),  the  torque  tending  to  rotate  will  be  yearly  6  ½  times  the  torque

developed by engine at its speed of 3000 rpm.

7

6

TORQUE  RATIO

100

5

4

80

EFFICIENCY

60

3

2

40

20

1

0

500

1000

1500

2000

2500

3000

OUTPUT SPEED REV / MIN

INPUT SPEED 3000 REV / MIN

If  the  resistance  to  the  motion  of  rotor  now  decreases,  so  that  rotor

starts  to rotate, then  as it  gathers speed so the driving torque driving action

on it falls off, At a rotor speed of 1000, f or eg: the driving torque would have

fallen off to about 3 times the engine torque, at 1900 rpm. The driving torque

would be just equal to engine torque, while at 2700 rpm, then driving torque

would have f allen to zero.

The efficiency on the other hand starts at zero, when the rotor speed is

zero,  because although torque  acting on the  rotor  is then larger,  no rotation

occurs and  torque does not  work,  thus  no  work is being  got out  of  converter

but a lot of  work  being put  in by  the engine  and so the  efficiency is  zero,  as

the  rotor  speed  increases, so  does  the efficiency  and  a  peak efficiency  of  86-

90% is reached at a rotor speed of about 1000 rpm.

As the  rotor speed  continuous to increase, the efficiency falls off again

and at 2700 rpm becomes zero one  more, this  time because  although rotor is

revolving  rapidly, the driving  torque on  it is zero,  and  no work can be  out of

it.

100

5

TORQUE  RATIO

4

80

EFFICIENCY

60

3

2

40

20

1

0 500 1000 1500 2000

OUTPUT SPEED REV / MIN

INPUT SPEED 2000 REV / MIN

The graph (b) shows the same things but for on impeller speed of 2000

rpm instead of 3000 rpm. It will be seen that the driving torque acting on the

rotor  when  it  is  stalled,  i.e.,  held  at  rest,  is  now  only  4  1/3  times  of  engine

torque  and  it  falls  of  to  zero  at  a  rotor  speed  of  1800  rpm.  The  efficiency

reaches a maximum value of only about 80% instead of 85-90%.It is thus that

only  a  rather  range  of  rotor  speeds,  if  the  efficiency  resonantly  good  and  it

must  be  borne  in  mind  that  if  efficiency  is  (say)60%,  then  40%  of  power

developed  by  engine  is  wasted,  being  converted  into  heat  which  raises  the

temperature  of  TC  fluid  and  which  has  to  dissipate  by  some  means,

commonly a radiator.

The falling off of the efficiency at low speed end of range can be treated

because these speeds  are  normally used  only  for  short period  when  starting

and climbing several hill, but the fall off at higher speeds cannot be tolerated

and must be circumvented.

There are two principle ways in which this can be done

a)  By substituting a direct drive for TC at high speeds.

b)  By making the TC function as a fluid flywheel at the higher speeds.

PRINCIPLE OF HYDRODYNAMIC TORQUE CONVERSION

The  phenomenon  of  torque  conversion  by  hydrodynamic  means  is

illustrated  graphically  by  polar  diagram,  where  distance  radially  outward

from the  base circle represent forward or positive  moments of momentum of

the  spinning  fluid  and  distance  inward  from  that  circle  negative  moments.

The spinning velocity of fluid and its moment momentum both are maximum

at  the runner entrance at the top of  diagram. When  the runner is at  rest  or

nearly  so  the  spinning  velocity  and  moment  of  momentum  of  the  fluid  are

quickly reduced to zero, and owing curvature of the running blades a reverse

or  negative spinning motion is  imparted  to  the fluid.  The torque imposed  on

the runner is proportional to the sum of the forward moment of momentum at

the  entrance  and  reverse  moment  of  momentum  at  the  exit  as  shown.  But

while  fluid  undergoes  a  great  change  of  motion  in  runner  and  as  a  result

subjects  the  latter  to  heavy  torque  it  gives  up  little  energy  to  the  runner

because latter is either standstill or  turning at  a  very low  speed.  On  leaving

the runner the fluid therefore still possesses most of  the kinetic energy with

which it entered the member.

In  reaction  member  the  spinning  motion  is  reversed  and

the  fluid  leaves  that  member  with  a  positive  moment  of  momentum  nearly

equal  to  the  negative  moment  of  momentum  with  which  it  entered.  The

reaction member is  subjected to a  torque opposite in direction to that on the

runner  and  proportional  to  the  difference  between  the  negative  moment  of

momentum at entrance and  positive moment of momentum at exit, of course

it  is  proportional  to  the  sum  of  the  two.  The  fluid  now  enters  the  impeller

already  possessed  of  a  certain  forward  spinning  velocity  and  the  impeller

needs to  add  only  enough  to  bring  the total  velocity  up to  that  at which the

fluid  entered  the  runner.  In  the  case  represented  by  the  diagram,  if  the

moment  of momentum  added to the  fluid  in the impeller is  represented by1,

the  change  of  moment  of  momentum  in  the  reactor  is  about  1.4,  and  the

change of  moment of momentum in the runner is 2.4.There fore torque ratio

in this particular case is 2.4.

UNIT III

AUTOMATIC TRANSMISSION

AUTOMATIC TRANSMISSION

It is the transmission which automatically provides varying gear ratios

to  suit  operating  conditions.  In  this  case  gear  changes  are  effected

automatically without manual assistant.

MAIN COMPONENTS OF AUTOMATIC TRANSMISSIO N SYSTEM

1. Torque converter.

2. Gearbox of planetary type with friction brake bands and multiple

disc       clutch operated by hydraulic system.

3. Hydraulic Control System. This system has a source of hydraulic

pressure servo units and control valves.

BLOCK DIAGRAM OF AUTOMATIC TRANSMISSION

ADVANTAGES OF AUTOMATIC TRANSMISSION SYSTEM

1. Smooth operation.

2. Ease of control, i.e. it relieves the driver from fatigue due to the

elimination of clutch and gear controls.

3. Numerous numbers of gear ratios are available.

4. Quick change of gear ratios effected automatically.

5. Minimum interruption of power during gear shifts.

DISADVANTAGES OF AUTOMATIC TRANSMISSION SYSTEM

1.  High cost.

2.  Complicated design.

3.  Possibility for oil leakage.

EPICYCLIC GEAR TRAIN

Sun gear (S) = 30 teeth (A)

Annulus (or) Ring gear (A) = 75 teeth (B)

SUN      = DRIVER

FOR

CARRIER = DRIVEN

HIGH REDUCTION

ANNULUS = FIXED

GEAR RATIO  A / (A+B) = 30 / (30 + 75)

GEAR RATIO = 3.5 : 1

SUN      = DRIVEN

FOR

CARRIER = DRIVER

LOW REDUCTION

ANNULUS = FIXED

GEAR RATIO  (A+B) / A  = (30 + 75) / 30

GEAR RATIO = 1.4 : 1

SUN      = DRIVER

FOR

CARRIER AND

DIRECT DRIVE

ANNULUS ARE

INTER LOCKED

WITH EACH OTHER

GEAR RATIO

GEAR RATIO = 1 : 1

SUN           = FIXED

FOR

CARRIER = DRIVER

OVER DRIVE

ANNULUS = DRIVEN

GEAR RATIO  (A+B) / A  = (30 + 75) / 30

GEAR RATIO = 1 : 1.4

SUN           = DRIVER

FOR

CARRIER = FIXED

REVERSE DRIVE

ANNULUS = DRIVEN

GEAR RATIO  A / B  = 30 / 75

GEAR RATIO = 2.5 : 1

SUN           = DRIVER

FOR

CARRIER = FREE

NEUTRAL

ANNULUS = DRIVEN

GEAR RATIO

GEAR RATIO = --

PRINCIPLE OF THE ALL-SPUR TYPE

One form of the “all-spur” type of planetary transmission is illustrated

in  diagram.    It  comprises  three  adjacent  independent  gears  A,  B,  D,

Concentric with the driving and driven shafts S and S’, which are telescoped,

and  three  corresponding  pinions  A’,  B’,  D’,  forming  a  rigid  planetary  unit.

There  are  usually  three  such  units,  spaced  uniformly  around  the  gears

mounted on  the driving and driven  shafts. Gear  A is the driving  and gear  D

the driven member.

Low  forward  speed  is  obtained  in  a  simple  manner  by  holding  the

planet carrier from rotation, by means of a brake drum provided on it for the

purpose.  Power then enters at gear A and is transmitted through the pairs of

back gears A’, D’, to gear D, hence no planetary motion is involved in the low

speed  forward  drive.    The  low-speed  reduction  ratio  is  a’d  /  ad’.    For  high

forward speed the driving shafts is coupled to the driven shaft by means of a

friction clutch incorporated in the assembly, which gives a direct drive.

For  the  reverse  motion  gear  B,  which  is  free  on  the  driving  shaft,  is

held  from  rotation.    Assume  that  the  planet  carrier  rotates  left-handedly,

causing  pinion  B’  to roll  on  B.   For one  left-handed  revolution  of  the  planet

carrier, the gear cluster A’, B’, D’, makes b/b’ left-hand revolutions around its

own axis. The  reduction  ratio  then is d (b-a)  / a (d-b).  It  will  be seen  at once

that this reduction is positive if b > a and d > b.

FORD T-MODEL

An example of the “all-spur” type of planetary transmission is the ford

model T, with which millions of cars have been equipped. A sectional view of

this  transmission  is  shown  in  figure.  Here,  instead  of  power  being  applied

through one of the sun pinions, it is applied to the planet carrier.

The  flywheel  rim  A  serves  as  planet  carrier  and  driving  member,

having lateral studs secured into it which carry triple planetary pinions. Gear

B is the  driven member, being keyed to the  hub  of clutch  drum  C, which  in

turn is secured to driven shaft D. By applying a brake band to drum E, gear F

is  held stationary, pinion G rolls on it, and the smaller pinion H causes  gear

B  to  turn  slowly  in  the  same  direction  as  pinion  carrier  A.  By  applying  a

brake band to drum I, gear J is held stationary; pinion H turns gear B slo wly

in the  reverse  direction. For the high  gear or direct drive, the  friction clutch

locks clutch drum C to the engine crankshaft, and the gear rotates as a unit.

The  three  pedals  control  the  transmission  and  brakes.  When  the  left

pedal  is  push  down  all  the way,  the car is low gear.  To remain  in low gear,

you must  continue  pushing  on  the left  pedal.  (It’s been  said that  you push a

Model T up a  hill in  low gear with your left foot!). If the left pedal is pushed

to  the  halfway  position,  the  car  is  in  neutral.  When  the  left  pedal  is

completely released (not depressed at all) , the car is in high gear. If the car is

in  neutral  (either  by  depressing  the  left  pedal  halfway  or  by  moving  the

leaver to the left of the pedals to an upright position) the middle pedal can be

pushed  to  engage  reverse  gear.  The  right  pedal  is  a  brake  that  acts  on  the

transmission  when  pushed.  Operating  the  brake  and  transmission  sounds

more difficult than it really is. After some practice, most drivers don’t give it

a second thought.

Interestingly,  the  Model  T  has  a  planetary  transmission  that’s  the

forerunner of the transmission. It’s very similar to an automatic transmission

expect you use foot pedal pressure to operate the bands rather then hydraulic

pressure and  it  doesn’t have  a  torque converter.  The leaver at  the right and

under the steering wheel is the hand throttle. It controls the speed, much like

the control found on the tractor or riding mower.

Model T’s were made  from 1908  until  1927. Over 15  million Model T’s

were  produced.  Far  more  were  produced  than  any  other  car  until  the

Volkswagen Beetle overtook its production in the 1970’s, at a time when two-

car families become the  norm. The impact of the Model T’s in its day is hard

far  us  to  imagine,  but  in  the  early  1920s,  half  of  all  cars  on  the  road

worldwide were Model T’s.A Model T in good mechanical condition will cruise

all day at 30 to 35 mph. Most can go 45 to 50 mph but the engine is working

pretty  hard  at  these speeds, so  most drivers  go  this  fast  only  briefly.  These

figures also depend upon the body style and weight of the car, with roadsters

and sedans and depot hacks the heaviest.

WILSON GEAR BOX

CONSTRUCTION

The  gearbox  comprises  of  three  subassemblies,  the  running  gear,  the

brake  harness  and  the  control  mechanism  housed  in  an  oil  tight  container.

This  consists  of  a  four  epicyclic  trains  of  gear  inter  connected,  so  that

different ratios and a reverse can be obtained. The direct drive is achieved by

engaging the clutch.

One train of epicyclic  gearing is used for  all the various ratios, its sun

S1 being secured to a shaft D coupled permanently to the engine and its arm

R1  to  the  shaft  E which is  coupled  permanently  to  the  driving  road  wheels

and  the  various  ratios  are  obtained  by  driving  the  annulus  A1  at  different

speeds in relation to the engine speed.

OPERATION

FIRST GEAR

First  gear  is  obtained  by  applying  a  brake  to  the  first  gear  train

annulus A1. So that it is held stationary. The engine will then, be turning the

sun gear S1. So that the planet gears will be rolling round inside the annulus

A1  carrying  their  arm  R1  round  with  them.  As  this  arm  R1  fixed  to  the

output shaft its motion is imported to it.

First Gear ratio:

Engine speed = 1000 rpm = sun S1 speed

Arm R1 speed = wheel speed   = 1000 x s/ (a +s)

= 1000 x 25 / (100 + 25)

= 200

Where    s = 25 = sun wheel teeth

a = 100 = annulus teeth

Gear ratio:

1000: 200

5: 1

SECOND GEAR

Second  gear  is  obtained  by  holding  the  second  gear  train  annulus  A2

stationary  by  its  brake.  The  main  sun  gear  S2  still  turned  by  the  engine

cause  the  planet  gear  to  revolve  and  their  arm  R2.  But  this  arm  R2  is

connected to the first  gear train annulus A1 which  therefore turns, speeding

up the rotation of  the planet gear and arm R1 and it turning the output shaft

faster than was the case in first gear, i.e. less reduction.

Second Gear ratio:

Engine speed   = 1000 rpm = sun gear S1

Annulus speed   = 100 rpm

Gear ratio:

1000  : 280

3.57 : 1

THIRD GEAR

Third gear is obtained by holding the third gear sun wheel S3 by brake

drum holding. Which is interconnected further the annulus A3 is an integral

part of the second gear planet arm R2 which is in turn connected to the first

gear  annulus  A1.  The  third  gear  arm  R3  is  connected  to  the  second  gear

annulus  A2  so  driving  it  in  same  direction  as  the  engine.  i.e.  increasing  its

speed so the drive is taken back through the second gear planets and arm R2

and the first gear train annulus A1 both of which are speeded up. The result

is  to  speed  up  the  first  gear  train  arm  R1  which  are  connected  to  output

shaft.  In  other  words  by  interconnecting  the  second  and  third  arms,  an

increase of speed is obtained at  the first gear train annulus, which increases

the speed of the arm R1.

Third Gear ratio:

Sun wheel S1 speed =   1000 rpm

Arm R1 speed    =   360 rpm

Gear ratio:      1000 : 360

2.78 : 1

TOP GEAR

In the top gear all the gear trains are locked together and revolve as a

solid block driving the output shaft at engine speed. This is brought about by

the engagement of this driving member to the clutch which  is the  drum and

sun  gear  S3  gear  train.  So  that  locking  the  third  gear  sun  to  the  driving

shaft.

Those are all the sun gear will be revolving at the same speed. Since the first

and second gear train sun wheel are fixed to the shaft (output) and their will

not  be  any  individual  action  of  the  various  gear  train.  All  the  brake  bands

being loose their annulus.

Gear ratio:

1000 : 1000

1 : 1

REVERSE GEAR

The first gear annulus A1 is connected to the sun gear S4 of the reverse gear train

and hence drive output shaft opposite to engine rotation. When the brake is applied to the

reverse gear annulus A4 the reverse gear planet wheels turned by the reverse sun gear

connected to the first gear annulus and therefore turning opposite to the engine speed

output shaft. As the arm A4 connected to the output shaft the direction of rotation of the

propeller shaft reversed.

Reverse Gear ratio:

Sun wheel S1    = 25

Annulus A1       = 100

Sun wheel S4    = 40

Annulus A4       = 80

Gear ratio:    7 :1

COTAL EPICYCLIC GEAR BOX

CONSTRUCTION

The wheel A is integral with the engine shaft and meshes with pinions

carried  by  a  spider  A  which  is  free  to  slide  along  the  outside  of  the  engine

shaft. When the spider B is slid to the left, its teeth E mesh with teeth F of an

annulus which is fixed to the gearbox casing. The pins of the spider then form

fixed  bearings  for  the  pinions,  and  so  the  annulus  C  with  which  the  latter

mesh is driven in the opposite direction to the wheel A. This gives the reverse

drives.  When the  spider B is slid to the  right its  teeth  E  engage  the teeth of

the annulus C and then the wheel A, pinions, spider B and annulus C revolve

‘solid’. This gives the forward drives.

The  four forward  ratios are  obtained by means  of  two epicyclic  trains

arranged in  tandem.  One  consists  of the  sun D (fixed to  the annulus  C), the

compound  planets P1, P2 (carried on the pins L of the arm which is integral

with the annulus H of the second train) and the annulus G which can be held

fixed.

When this is done the annulus H is driven in the same direction as the

sun  D but at a lower speed. The  second train  consists  of the  annulus H, the

sun  K  and  the  arm  J  which  is  fixed  on  the  output shaft.  The  sun  K  can  be

held  at  rest  so that  the train  gives  a  reduction  between the  annulus H  and

the arm J and it can also be locked to the output shaft so that the train must

revolve solid. The annulus G can also be locked to the sun D so that the first

train must revolve solid.

WORKING

The  fixing  and  locking  of  the  members  is  done  by  electromagnets

whose windings S1 S2 S3 S4 are energized as may be required. For first gear

S2  and  S3  are energized  and  both  epicyclic  trains  provide  a  reduction  since

both  annulus  G  and  sun  K  are  fixed.  For  second  gear,  S2  and  S4  are

energized and the second train revolves solid, the only reduction being in the

first  train.  For  third gear,  S1 and  S3  are energized,  the  first  train  is  locked

solid  and  the  only  reduction  occurs  in  the  second  train.  For  f ourth  gear  S1

and S4 are  energized  and both trains revolves solid  so that  a direct  drive  is

obtained.

The windings S1and S4 are carried by parts that sometimes rotate and

so  these  windings  are  connected  to  slip  rings  on  which  brushes  bear.  The

current for energizing the windings is supplied by the battery or generator of

the car and is between two and three amperes.

The  control  is  extremely  simple  consisting  merely  of  a  switch  which

connects  the  appropriate  winding  to  the  battery.  This  switch  is  usually

mounted at the center of the steering wheel.

AUTOMATIC OVER DRIVE

PRINCIPLE OF THE OVER DRIVE

The  principle  of  the  overdrive  is  illustrated  in  figure,  which  shows  a

simple epicyclic gear train.  In this the  gear  box output shaft is  connected to

the planet carrier ring while the annulus or ring gear is attached to the outer

race of the free-wheel unit and from this to the output shaft; the latter drives

the propeller shaft through the front universal coupling. The sun wheel is the

reaction  member  of  the  gear  train  and  when  it  is  locked  to  the  gear  box

output -or overdrive input-shaft the planet carrier which is driven by the gear

bow  shaft  rotates  about  the  sun  wheel  carrying  with  it  the  pinion  wheels

which  in  turn,  drive  the  annulus  gear  and  with  it  the  output  shaft  to  the

propeller shaft. The annulus rotates more slowly than the planet carrier thus

giving a lower gear ratio  than for direct drive. The position in which the sun

wheel is locked to the gear box shaft, which has just been described, gives the

overdrive requirements.

OVER DRIVE OPERATIONS

DIRECT DRIVE CONDITIONS

To  obtain  direct  drive  the  overdrive  gear  must  be  locked  in  some

manner  so  as to rotate as  one solid  unit.  This  is done by  connecting the  sun

gear solidly with the planet carrier. The drive from the gear box shaft is then

taken  through  the  locked  epicyclic  gear  train  and  thence  through  the  free-

wheel  to  the  overdrive  output  shaft.  Therefore,  when  in  direct  drive  the

propeller shaft side can rotate faster than the gear box shaft. Since, however,

the  direct  drive  is  only  used  at  speeds  below  about  28  to  30  m.p.h,  this

advantage is only realized at these at these lower speeds.

COMPLETE OVERDRIVE

Having  explained  the  principle  of  this  overdrive,  the  purposes  of  the

various  components  should  be  better  understood  by  reference  to  the

illustration  of a  complete  overdrive,  as  used on  cars fitted  with  three-speed

gear boxes. The annulus or ring gear and the outer race of the free-wheel are

splined to the overdrive main shaft.

The  overdrive  unit  includes  a  device to  lock  the sun gear  and  hold  of

stationary.  To do this a centrifugal go vernor,  driven  by the o verdrive output

shaft  is  used to close  the contacts of  an  electrical  circuit  which  contains  the

windings  of  the solenoid. When the  road speed of  the car increases to  about

28  to  30  m.p.h.,  the  governor  closes  the  contacts  and  thus  energizes  the

solenoid  which  forces  its  plunger  outwards  and  therefore  pushes  the  pawl

member towards a notched ring around the overdrive input shaft; this pawl is

shown  as  the  gear  plate.  Since  if  would  not  be  advisable  for  the  pawl  to

engage  with  one  of  the  notches  in  the  gear  plate  during  the  rotation  of  the

plate the pawl of not allowed, initially, to enter a notch, being prevented from

doing so by a baulk ring which is a friction fit to the gear plate.

To  obtain  a  smooth  engage ment  of  the  pawl  it  is  necessary  to

decelerate  the  overdrive  input  shaft,  momentarily,  by  releasing  the

accelerator  pedal,  so  that  the  engine  begins  to  slow  down.  Since  the

momentum of the car will cause the ring gear still to rotate, the ring gear will

rotate the pinions, driving the sun gear and baulk ring in a reverse direction.

This movement of the baulk ring allows the pawl to move from the  step and

engage  one  of  the  gear  plate  notches,  thus  bringing  the  overdrive  into

operation.  The  engagement,  after  the  accelerator  pedal  release,  is  so  quick

that  the  gear  plate   rotates  only  about  one-third  of  a  turn  before  full

engageme nt  of  the pawl  with  a  notch.  This  method  of  engagement  depends

upon synchronizing  the pawl movement  with the momentary stopping of the

gear plate.

To release  the overdrive the accelerator should be released so that the

road speed falls by 2 to 4 m.p.h below the cut-in speed; so that the governor’s

contacts open  and the  solenoid  actuated pawl  is  released;  the direct  drive  is

then re-engaged, automatically.

LOCKING THE OVERDRIVE

As  mentioned  earlier,  in  order to  obtain  normal  top  gear  as  given  by

the gear box, it is necessary to lock the epicylic gear so that it will rotate as a

solid  unit.  The  sun  gear  which  is  integral with  the  pinion shaft is therefore

locked to the planet carrier and the while unit revolves solidly.

THE KICK-DOWN CONTROL SWITCH

When  the  car  is  running  in  overdrive,  due  to  the  fact  that  the  gear

ratio is then lower than for direct top gear there is, at any given speed, below

maximum, less engine power available for the overdrive than for direct drive

at the same speed. Therefore, should the driver wish to accelerate, for traffic

passing  purposes,  it  is  possible  for  him  to  do  so,  simply  by  depressing  the

accelerator  pedal  quickly  and  to  its  full  extent.  The  result  is  to  release  the

solenoid  current but owing to  the torque reaction the pawl does not leave its

notch  in  the  gear  plate  and  cannot  do  so  until  the  torque  is  released

momentarily. This is done with the kick-down switch which is operated when

the accelerator pedal is depressed fully, thus switching off the ignition so that

the  pawl  readily leaver its  notch and  also  the gear plate; the  direct  drive  is

then in operation through the over running clutch.

When  the  driver  wished  to  return  to  the  overdrive he lifts  his  foot from  the

accelerator  pedal  for  a  few  seconds,  when  the  over  drive  engages

automatically,  unless  the  car  speed  falls  below  about  28  to  30  m.p.h.For

convenience the overdrive switch is of ten mounted on the carburettor, so that

it  can  be  actuated  by  the  accelerator  pedal  rod  connection  at  the  throttle

lever.

SOLENOID UNIT

The  solenoid  comprises  (i)  a  heavy  traction  type  of  winding  which  is

provided to mo move the  plunger outwards until the pawl is almost engaged

with  the  gear  ring;  (2)  a  hold-in  winding  taking  much  less  current  than  (i)

which holds the plunger in its outward position; (3) relay contacts.

One set of contacts operates when the governor switch closes at 28 to

30  m.p.h., the  other contacts  in  series  with  the  windings  (i)  opens  and  cuts

out  these  windings.  Since  the  solenoid  remains  energized  during  the  whole

period  of  over  drive  engagement  the  current  consumption  is  reduced

appreciably since it flows through the holding winding, only.

ELECTRICAL CIRCUITS

There are three circuits associated with the operation of the overdrive,

the circuits are shown diagrammatically.

THE CONTROL CIRCUIT

This circuit includes the solenoid relay and the electrical contacts in the kick-

down  and  governor  switches.  These  two  contacts  must  be  closed  for  the

solenoid  to  operate.  The  relay  is  a  type  of  switch  operated

electromagnetically,  such  that  when  current  flows  through  a  relay  winding

the  relay  contacts  are  closed.  If  either  of  the  other  two  set  of  contacts  are

opened, the relay contacts will be broken.

THE SOLENOID CIRCUIT

This circuit includes the  solenoid winding  and  also the  relay contacts.

When  the contacts  are closed the  solenoid pull–in winding  is  energized, and

the pawl is moved towards the notched ge ar ring as explained earlier. As the

solenoid plunger completes its outward movement it opens a set of contact in

series  with  the  pull-in  winding.  The  current  in  the  pull-in  winding  is  thus

switched  off  and  at  the  same  time  currents  is  switched  on  to  the  holding

winding to keep the solenoid plunger in its outward position.

THE KICK-DOWN OR IGNITION CIRCUIT

This  circuit,  which  is  indicated  by  the  dotted  lines  in  figure,  is

connected  in  parallel  with  the  ignition  distributor’s  contact  breaker  points.

Its  also  includes  the  normally  open  solenoid  contacts  which  close  when  the

overdrive is engaged. When the kick down switch is operated the ignition coil

primary winding is earthed through these two sets of contacts thus cutting off

the ignition  H.T  current to the  sparking plugs and  thus  stopping  the engine

momentarily.  The  control  circuit  is  opened  at  the  same  time,  to  allow  the

overdrive to be cut out of action as explained previously.

ADVANTAGES OF OVER DRIVE

1.  This device  permits the engine to operate at  only about 70%  of the

propeller shaft speed when the car is operating in the higher speed

ranges. i.e., over drive engine speed about 30%.

2.  Because  the  engine  is  not  required  to  turn  over  fast  at  high  car

speed, the use of over drive reduces engine wear and vibration and

saves gasoline.

3.  Usually a slightly higher rear –axle  gear ratio is employed with an

over –drive then without one.

DRAWBACKS OF OVER DRIVE

1.  In descending long steep hills where the braking effect of the engine

would  be  lost  due  to  slip  in  ORC.  To  avoid  over  drive  should  be

locked.

2.  The  driving force available at  the wheels  is  less  in case of  vehicles

with over-drive.

REVERSE LOCK-UP

Since the free-wheel unit cannot power in reverse, provision is made in

the  Gear-shift  linkage  to  shift  the  rail  and  fork  assembly  into  the  lock-up

position whenever the conventional transmission is shifted take reverse gear.

OVER-DRIVE LUBRICATION

The over-drive unit is connected to the transmission and uses the same

type of lubricant, SAE 80 (or) 90 gear oil (or) SAE Engine Oil.

OVER-DRIVE GEAR RATIO

Driving member    -  Planet Carrier (A)

Driven member    -  Ring Gear (R)

Fixed member    -  Sun Gear (S)

RING GEAR  SUN  ARM

S/R  -1  0

1  1  1

(R+S) / R  0  1

Over-Drive gear ratio   =   Driving / Driven

=   1 / ( ( R+S ) / R )

=   R / ( R+S )

If number of teeth in ring gear is 140 and sun gear are 60.

Then,

The Over-Drive gear ratio  =140 / ( 140 + 60 ) = 0.7.

=  0.7 : 1

HYDRAULIC CONTRO L SYSTEM

The  hydraulic  control  system  of  the  automatic  transmission  is shown

in  figure.  Which  is  a  simplified  diagram  illustrating  the  basic  principles.

Hydraulic fluid is drawn from input and ensures that pressure is available as

soon as the engine  starts. The  rear pump  is driven  from the  output  shaft so

that  pressure  is  generated  in  this  pump  as  soon  as  the  vehicle  moves,  and

this  feature  provides  a  means  of  preventing  the  reverse  and  park

mechanisms being engaged whilst the vehicle is in motion. Non-return valves

ensure  that  hydraulic  pressure  can  be  available  from  either  pump  and  the

joint  delivery  is  regulated  to  a  suitable  pressure  by  a  pressure  relief  valve.

The  fluid  at  regulated  pressure  is  fed  to  the  converter  which  is  kept  full  of

fluid  and  a  small  flow  from  the  converter  is  used  for  lubrication  of  the

gearbox.

The  main  fluid  supply  is  fed  to  the  manual  selector  valve  which  is

controlled by a steering-column selector lever, and this may be moved to any

of  five  positions.  This  valve  may  direct  fluid  under  pressure  to  the  reverse

brake when a reverse ratio is obtained. In the low selection, fluid is applied to

both the forward and low brakes and maintains the transmission in low gear.

Neutral  selection  is  obtained  by  removal  of  pressure  from  all  friction

elements,  and  the  park  position  engages  a  mechanical  lock  preventing

rotation of the output shaft.

When  the  Drive  selection  is  made  the  manual  selector  applies  fluid

under  pressure  to  the  Forward  and  Low  brakes  and  also  to  the  governor

valve.  The  governor  valve  is  moved  by  the  combination  of  an  accelerator

pedal  movement  together  with the  position of a centrifugal  governor. At  low

road speeds the governor valve is blocked and the transmission is retained in

low  gear.  At  a  higher  road speed  the governor  valve  moves  to apply fluid  at

pressure to  the multi-plate  clutch  so  as to engage  Intermediate gear. As the

multi-plate clutch begins to take up the drive the pressure in the clutch rises

and becomes sufficient to operate the relay valve and cut off the fluid supply

to the low friction brake band. This relay valve carries out the transition from

Low  to  Intermediate  clutch.  This relay valve corresponds to  the  more usual

shift although in this case the valve is moved by spring force in opposition to

hydraulic pressure.

The  change  into  direct  drive  is  effected  by  the  application  of  fluid

pressure  to  the  single-plate  clutch  by the  governor  valve. The  other  friction

elements  remain  in  the same  condition  as for the  Intermediate gear  so  that

no  transition from one  element to another is needed. No smoothing device  is

incorporated for the take-up of this clutch, which relies on the capacity of the

clutch  piston  to  give  a  steady  build-up  of  pressure.  Gear  changes  to  lower

ratios operate in the reverse sequence.

The  complete  hydraulic circuit  diagram  is  only  slightly different  from

the  simplified  block  diagram  and  a  typical  system.  It  will  be  noted  that  a

hydraulic  accumulator  is  included  to  give  a  rapid  initial  flow  of  fluid  when

the selector or governor valves operate, and a converter shuffle valve adjusts

the converter pressure to a higher valve in low gear. A small hydraulic detent

applies a slight bias to the  governor valve so that  hunting,  or  repeated  gear

changes  between  two  ratios,  is  avoided.  Interlocks  are  provided  to  prevent

engageme nt  of  the  mechanical  Park  interlock  mechanism  when  the  rear

pump  is  generating  pressure,  indicating  movement  of  the  output  shaft.  A

similar  interlock  piston  prevents  Reverse  gear  being  engaged  when  rear

pump  pressure  is  available.  This  piston  operates  so  as  to  block  the  control

line which supplies  pressure to  the Reverse servo  pistons. The  relay valve  is

restored  by  hydraulic  pressure  to  ensure  a  rapid  operation  of  the  piston

return spring when a manual selection of low is made

HYDRAULIC COMPONENTS

A  summary  of  the  functions  of  the  various  hydraulic  components  is

given in an abbreviated manner.

Front  Pump:  Driven  from  input  shaft  and  provides  the  main  hydraulic

supply.

Rear Pump: Driven by output shaft and acts as an auxiliary supply in case

of front pump failure, and also to detect forward movement of the vehicle.

Pressure  Relief  Valve:  Regulates  hydraulic  supply  pressure  from  both

pumps to predetermined values. Initially, the relief valve springs ensure that

20  lb. /sq. in. pressure  is admitted to the  back  of the  relief valve  raising the

system  to  80  lb.  /sq.  in.  which  is  the  normal  pressure.  When  Reverse  is

selected,  hydraulic  pressure  is  applied  to  another  piston  so  as  to  raise  the

pressure to 200 lb. /sq. in

Ball  valves:  Two balls inserted in  the main supply line  prevent  a  failure of

either  pump  causing  a complete loss  of pressure.  The  system is arranged so

that  either  pump  will  supply  the  control  system  as  soon  as  the  vehicle  is

moving.

Hydraulic Accumulator:  Spring deflects  when pressure is applied and the

accumulator piston retracts in the cylinder to store a small volume of fluid at

pressure.  At a given deflection of the  piston,  fluid is  admitted to the  back of

the pressure relief valve to increase the regulated pressure.

“Park”  Interlock:  A  small  spring  loaded  piston  deflects  due  to  pressure

from the rear pump to prevent engagement of the Park lock.

Reserve  Interlock  Valve:  A  spring  loaded  piston  deflects  due  to  pressure

from  the  rear  pump  to  prevent  pressure  being  applied  to  the  Reverse  band

brake.

Manual Selector Valve: operated by the selector lever for the five positions:

park, netural, drive, low and reverse.

“Park,”  “Neutral”  positions:  All  pressure  is  cut  off  from  the  friction

clutches  and  bands. The park mechanism is operated from the  selector lever

but will not engage if the vehicle is moving forwards.

“Drive”  position:  Pressure  is  applied  to  the  forward  and  low  band  brakes

and also to the governor valve.

“Low” position: Pressure is maintained on the forward and low bands but is

removed from the governor valve and applied to the back of the relay valve.

Governor  valve:  Operated  by  a  combination  of  road  speed  (as  measured

from  the  output  shaft),  together  with  the  accelerator  pedal  position.  The

valve  initiates  the  gear  changes  between  low  and  intermediate  ratios  and

between  intermediate  ratio  and  direct  drive  at  predetermined  speeds  when

the manual selector valve has been moved to drive.

Converter  shuttle  valve:  Regulates  the  flow  of  fluid  into  the  hydraulic

converter-coupling. Fluid  is  supplied from  the  main  supply line  to  the  valve

and  flows  through  a  conical  shaped  valve  seat.  When  reverse is selected,  or

when  intermediate  or  direct  gear  is  operative  the  pressure  applied  to  the

converter  by inserting a conical  plug  into  the valve seat so that an orifice of

reduced size is presented to the flow. An increased pressure, and hence, flow

is permitted for the low selection.

“Reverse” Position: Pressure  is applied to the Reverse band brake, via the

interlock  valve.  Pressure  is  also  applied  to  the  converter  shuttle  valve  and

the main relief valve.

Lubrication  valve:  The  fluid  drive  is  maintained  at  pressure  by  a  spring

loaded ball valve. When the pressure exceeds the set value the balls lifts and

permits  a  flow  of  fluid through the  converter.  The escaping  fluid is used  for

lubrication of the gearing.

Clutch  Pistons:  The  single  plate  friction  clutch  and  the  multi-plate

Intermediate  clutch  are  both  operated  by  annular  pistons  which  fit  in

appropriate housings and apply the necessary load to the friction plates when

fluid pressure is available.

Brake Pistons: The friction band brakes are applied by servo pistons which

develop  the  necessary  loads  to  hold  the  brake  drums  stationary.  The  servo

cylinders each contain two pistons which act in tandem. A small restriction is

placed between the two pistons as a means of smoothing the application and

release of the bands.

UNIT – IV

HYDROSTATIC DRIVE AND ELECTRIC DRIVE

HYD ROSTATIC DRIVE

In this type  of drives  a  hydrostatic pump  and  a motor

is used. The engine drives the pump and it generates hydrostatic pressure on

the  fluid.  The  pressurized  fluid  then  fed to  the  motor  and the motor  drives

the  wheel.  In  these  transmissions  mechanical  power  is  generated  in  the

motor  as  a  result  of   displacement  under  hydraulic  pressure.  The  fluid,  of

course, also carries  kinetic energy, but since  it leaves the motor at  the same

velocity  as  that  at  which  it  enters,  there  is  no  change  in  its  kinetic- energy

content, and kinetic energy plays no part in the transmission of power.

PRINCIPLE OF HYDROSTATIC DRIVE SYSTEM

LAYOUT OF HYDROSTATIC DRIVE SYSTEM

It  consists  of  a  pump,  which  converts  torque  and  rotation  of

mechanical  shaft  into  flow  of  pressurized  f luid  combined  with  a  hydraulic

motor,  which  converts  fluid  flow  under  pressure  into  rotating  torque  on  the

output shaft. The pump and motor are identical in construction but they may

vary  in  size  and  displacement,  particularly  when  torque  multiplication  is

needed.  By  employing  variable  delivery  of  hydraulic  units,  it  is  possible  to

obtain a wide range of output ratios.

VARIOUS TYPES OF HYDROSTATIC SYSTEMS

1.  CONSTANT  DISPLACEMENT  PUMP  AND  CONSTANT

DISPLACEMENT MOTOR

Here  both  of  the  pump  and  motor  are  constant  displacement  type.

Hence, variation of  output torque or speed  is not  possible.  So,  this system  is

not  used.  This  system  suffers  loss  of  power  due  to  the  provision  of

intermediate  relief  valves.  Such  a  transmission  is  similar  to  a  very  flexible

mechanical  drive  shaft  except  for  slight  speed  loss  as  load increases  due  to

slip both in the pump and in the motor.

2.  VARIABLE  DISPLACEMENT  PUMP  AND  CONSTANT

DISPLACEMENT MOTOR

With a variable displacement pump and fixed displacement motor, it is

possible  to obtain  variable  output speed from  motor,  which can be smoothly

controlled from the designed maximum value to zero. This system provides a

constant output torque throughout the speed range.

It can be used to drive one or more hydraulic motor, and it gives equal

performance  in  both  forward  and  reverse  speeds.  Power  output  varies  in

direct  proportion  with  output  speed.  This  system  can  be  advantageous  in

tractors  and  construction  equipments.  With  the  pump  at  zero  output  an

idling  condition  is  produced which  is analogous  to a  disengaged  clutch.  The

transmission  can  be  reversible  without  the  need  for  a  directional  control

valve simply by reversing the pump.

Pump displacement

Motor displacement

Speed

in cc

in cc

ratio

0  0  0

75  375  5

375  375  1

3.  CONSTANT  D ISPLACEMENT  PUMP  AND  VARIABLE

DISPLACEMENT MOTOR

Fixed displacement pump and variable speed motor, capable

of  giving  constant  power  output,  which  is  independent  of  output  speed.

Output  torque and  speed  can  be  continuously  varied.  This  transmission  can

be  used  with  advantages  along  with  a  governed  engine  to  ensure  the

application of constant input power to transmission.

Crank radius of  pump  is fixed. So, displacement 375 cc is governed  at

maximum  BHP  level. If  power  is more  important than torque  this system  is

applied in such situations.

4.  VARIABLE  DISPLACEMENT  PUMP  AND  VARIABLE

DISPLACEMENT MOTOR

This combination can give either a constant power or a constant torque

drive. A wide range of speed variation may be obtained, the maximum motor

speed  being  with  the  pump  at  full  output  and  the  motor  at  minimum

displacement per revolution and vice-versa for minimum speed.

The  torque  capacity  is  in  inverse  proportion.  Since  both  are  variable

type,  the torque  ratio can be varied  widely.  When both the  pump and motor

are of  variable displacement type, possibilities of  infinite  variation  of output

speed and output torque are available.

ADVANTAGES OF HYDROSTATIC DRIVE

1.  Hydrostatic  drive  eliminates  the  need  for  mechanical  transmission

components like clutch and gearbox as well as allied controls.

2.  It provides for smooth and precise control of vehicle speed and travel.

3.  This system ensures faster acceleration and deceleration of vehicle

4.  It offers better flexibility in vehicle installation because of wide range

in  choice  of  pumps  and  motors  of  different  capacities  and  of  fixed  or

variable  displacement  type.  Besides  hydraulic  fluid  pipes  lines  replace

mechanical transmission drive line components

5.  The  ease  with  which  the  reverse  drive  can  be  obtained  makes  the

hydrostatic  drive  more  attractive.  This  drive  is  fully  reversible  from

maximum  speed in  one direction  to  zero speed  and to  maximum speed in

the reverse direction.

LIMITATIONS OF HYDROSTATIC DRIVE

1.  Noisy in operation

2.  Heavier in weight and larger in bulk

3.  Costlier when compared to other types of transmission

4.  Manufacturing  of  pump  and  motor  requires  high  precision

machining of components and skilled workmanship

5.  In  view  of  high  pressure  employed  in  system,  the  working

components  are  heavier.  It  also  possesses  problem  of  oil

leakage through oil seals.

APPLICATIONS OF HYDROSTATIC DRIVE

1.  It is used to move the machine tools accurately.

2.  Used in steering gears of ship.

3.  Used in war ships to operate gun turrets.

4.  Used in road rollers, tractors, earth movers, heavy duty trucks.

COMPARISON OF HYDROSTATIC DRIVE WITH HYDRODYNAMIC

DRIVES

1.  Torque ratio is lesser in hydrostatic drives for different speed ratios

2.  Hydrostatic  offers  high  efficiency  over  a  wide  range  of  speeds  when

compared to hydrodynamic drives.

3.  Vehicle  with  hydrostatic  drive  has  no  tendency  to  creep  unlike

hydrodynamic drive during idling.

4.  Dynamic braking of vehicle is an inherent feature of hydrostatic drive.

This  feature  helps  to  eliminate  conventional  shoe  or  disc  type  of

brakes.  Creep  is  caused  to  drag  torque,  movement  of  vehicle  during

idling

5.  Throughout the operating torque range, the vehicle operates at almost

constant  speed,  whether  the  vehicle  is  moving  uphill  or  downhill  or

when the load is suddenly removed.

6.  Pressure  relief  valve  as  a  basic  part  of  any  hydrostatic  transmission

and this provides complete overload protection to the engine as well as

hydraulic system.

JANNEY HYDROSTATIC D RIVE

CONSTRUCTION AND WORKING

A hydraulic  transmission  known  as  the  Janny  has  long  been  built  by

the Waterbury Tool Co. of Waterbury, Conn., for various industrial uses, and

it has been applied also to motor trucks, rails and diesel locomotives.

PUMP: Nine cylinders, axially disposed, variable stroke, swash plate type.

MOTOR: Nine cylinders, axially disposed, swash plate type, constant stroke.

A longitudinal section through the whole assembly is shown in figure.

Practically the only difference between pump and motor is in former inclination of

swash plate is adjustable while in latter it is not. Referring to the drawing Both the

pump and the motor unit have central shafts which project at one end only, each

shaft is supported by plain bearing in housing and a roller bearing in valve plate. To

the inner end of shaft is keyed, a cylinder block in which there are 9 bores forming

the working cylinder. The bores are parallel with the axis of rotation and equally

spaced around it.

When the cylinder block revolves, cylinder head slide against the valve

plate. A port in each of cylinder head registers alternatively with two annular

ports  in valve plate  for admission and delivery of oil, respectively. Each port

extends  over  approximately  125º,  and  since  there  is  port  opening  from  the

time the cylinder port begins to register with the valve plate port to the time

it passes out of registry therewith port opening extends over nearly 180º.

The  spring  surrounding  the  shaft,  serve  to  press  the  cylinder  block

against  valve  plate  when  no  load  is  transmitted.  During  transmission  of

power, the  fluid  pressure keeps all  parts in  close  contact. The cylinder block

is  so  mounted  on  the  shaft  that  it  can  slide  thereon,  and  also  it  can  rock

slightly.  This  enables the  block to seat  correctly on valve  plate even if  there

should be slight misalignment, or if wear should have occurred.

The plunger is lapped into bores to a clearance of 0.001”. Each plunger is

connected to socket ring by a connecting rod with spherical heads. The rods have

drill holes extending through their shanks, and there is a small drill hole also in the

head of the piston, hence the bearings of the connecting rod are lubricated with the

oil in the power transmission circuit, and the pressure under which lubricant is

supplied to the bearing surfaces is proportional to the load.

Each socket ring is connected to shaft by means of universal joint, so that

while it revolves with the shaft, its plane of rotation may bear any angle with the

axis of the shaft. In case of pump unit, angle of socket ring can be varied between

0deg and 20deg in either direction by means of control lever connected to roller

bearing tilting box. In motor unit, the angle box is secured to housing and has a

fixed inclination of 20deg.

PUMP

If  the  angle  box  is  set  of  right  angles  to  the  shaft,  there  will  be  no

reciprocation  of  plungers  in  cylinder  when  cylinder  block  is  revolving,  and,

consequently,  no  oil  will  be  moved.  When  the  angle  box  is  set  to  make  an

angle  with  the  shaft,  the  plungers  begins  to  reciprocate  in  the  cylinders  as

they revolve around with the block. Each cylinder draws oil through the port

in  valve  plate  during  one  half  of  the  revolution  and  delivers  oil  through

delivering port in valve plate during next half of revolution.

MOTOR

The  motor  unit  is  merely  an  inversion  of   the  principle  of  the  pump

unit,  oil  entering  the  cylinder  under  pressure  forcing  the  plunger  outward

and the reaction between socket ring and swash plate causing cylinder block

and  its  shaft  to  revolve.  If  the  angle  plate  of  pump  unit  is  set  to  the  same

angle as that of motor unit, then the motor will turn the same speed as pump

unit and any speed lower than this can be obtained on motor shaft by merely

reducing the angularity of auto angle box.

HYDROSTATIC TRANSMISSION

INTRODUCTION

Hydrostatic  transmissions are  hydraulic systems specifically designed

to have a pump to drive a hydraulic motor. Thus, a hydrostatic transmission

simply transforms mechanical power into fluid power and then reconverts the

fluid  power  back  into  shaft  power.  The  advantages  of  hydrostatic

transmissions include power transmission to remote areas, infinitely variable

speed  control,  self-overload  protection,  reverse  rotation  capability,  dynamic

braking,  and  a  high  horsepower-to-weight  ratio.  They  are  used  in

applications  where  lifting,  lowering,  opening,  closing,  and  indexing  are

required.  Specific  applications  include  materials  handling  equipment,  farm

tractors, railway locomotives, buses, automobiles, and machine tools.

A  system  consists  of  a  hydraulic  motor,  and  appropriate  valves  and

pipes  can  be  used  to  provide  adjustable-speed  drives  for  many  practical

applications.  Such  a  system  is  called  a  “Hydrostatic  Transmission.”  There

must,  of  course,  be  a  prime  mover  such  as  an  electric  motor  or  gasoline

engine.  Applications  in  existence  include tractors,  rollers,  front-end  loaders,

hoes, and lift trucks. Some of the advantages of hydrostatic transmissions are

the following:

1.  Infinitely  variable  speed  and  torque  in  direction  and  over  the  full

speed and torque   ranges.

2. Extremely high horsepower-to-weight ratio.

3. Ability to be stalled without damage.

4. Low inertia  of rotating members permits fast  starting and stopping

with smoothness and precision.

5. Flexibility and simplicity of design.

The  internal  features  of  a  variable  displacement  piston  pump  and

affixed  piston  motor  used  in  a  heavy–duty  hydrostatic  transmission.  Both

pump  and  motor  are  of  the  swash  plate  in-line  piston  design.  This  type  of

hydrostatic  transmission  is  expressly  designed  for  application  in  the

agricultural,  construction,  materials-handling,  garden  tractor,  recreational

vehicle and industrial markets.

The  operator  has  complete  control  of  the  system,  with  one  lever  for

starting,  forward  motion,  or  reserve  motion.  Control  of  the  variable

displacement pump  is the key to controlling  the vehicles. Prime mover horse

power  is  transmitted  to  the  pump.  When  the  operator  moves  the  control

lever,  the  swash  plate  in  the  pump  is  tilted  from  neutral.  When  the  pump

swash plate is tilted,  a positive  stroke of  the pistons  occurs. This, in turn,  at

any  given  input  speed, produces a  certain  flow  from  the pump.  This  flow  is

transferred through high pressure lines to the motor. The ratio of the volume

of flow from the pump to the displacement of the motor determines the speed

at  which the  motor  will  run. Moving the control lever to the opposite  side of

neutral  causes  the  flow  through  the  pump  to  reverse  its  direction.  This

reverses  the  direction  of  rotation  of  the  motor.  Speed  of  the  output  shaft  is

controlled by adjusting the displacement (flow) of the pump.

Load  (working  Pressure)  is  determined  by  the  external  condition

(grade,  ground  conditions,  etc.),  and  this  establishes  the  demand  on  the

system.  The  shutoff  valve  is  included  to  facilitate  a  filter  change  without  a

large  loss  of  fluid  from  the  reservoir.  The  heat  exchange  ensures  that  the

maximum continuous oil temperature will not exceed 180°F.

OPEN TYPE ONE WAY HYDROSTATIC TRANSMISSION

There  are  two  types  of  hydrostatic  transmission  system.  They  are

closed and open circuit drives. In open circuit drive the pump draws its fluid

from  the  reservoir.  Its  output  is  then  directed  to  a  hydraulic  motor  and

discharge  from  the  motor  back  into  the  reservoir.  In  a  closed  circuit  drive,

exhaust oil from the motor is returned directly to  the pump  inlet. The figure

gives  a  circuit  of  a  closed  circuit  drive  that  allows  foe  only  one  direction  of

motor  rotation.  The  motor  speed  is  varied  by  changing  the  pump

displacement.  The  torque  capacity  of  the  motor  can  be  adjusted  by  the

pressure setting of the relief valve. Makeup oil to replenish leakage from the

closed loop flows into the low-pressure side of the circuit through a line from

the reservoir.

CLOSED TYPE REVERSIBLE HYDROSTATIC TRANSMISSION

Many  hydrostatic  transmissions  are  reversible  closed  circuit  drives

that use a variable displacement reversible pump. This allows the motor to be

driven in  either direction  and at  infinitely variable  speeds depending on the

position of the pump displacement control. The Figure shows circuit of such a

system  using  a  fixed  displacement  hydraulic  motor.  Internal  leakage  losses

are made up by a replenishing pump, which keeps a positive pressure on the

low-pressure side of the system. There are two check and two relief valves to

accommodate the two directions of flow and motor rotation.

ELECTRIC DRIVE

Electric  drive  equipment  for  transportation  units  consists  of  a

generator driven by the prime mover, a motor or motors  in direct connection

with  the  driving  wheels  of  the  unit  and  supplied  with  current  from  the

generator and the necessary control  apparatus. In locomotives the generator

is  separately  excited,  as  a  rule,  and  the  equipment  then  includes  a  small

additional generator, the exciter.

PRINCIPLE OF ELECTRIC TORQUE CONVERSION

With  electric  drive,  speed  control  of  the  vehicle  can  be  done  either

electrically  or  by  varying  the  speed  of  prime  mover.  In  the  first  the  engine

and direct connected generator operate at constant speed under the control of

a  governor.  This  system  was  in  favor  during  pioneer  days,  when  gasoline

engines  had  very  little  flexibility.  The  other  system,  in  which practically  all

speed control of the vehicle is effected by means of the engine throttle or fuel

control rack was used exclusively during the later days of bus electric drive.

EARLY WARD LEONARD CONTROL SYSTEM

An early method of obtaining a variable speed drive electrically from a

constant  speed  prime  mover  is  known  as  the  Ward  Leonard  system.  It

comprises a generator whose field current is obtained from a separate exciter.

Generator  terminals  are  directly  connected  to  the  terminals  of  the  motor,

whose field is also separately excited, from the same source as the generator

field. But whereas the field of the motor is at all times excited to the point of

saturation,  the  field  current  of  the  generator  is  controlled  by  means  of  a

rheostat.

With  the  generator  driven  at  constant  speed,  its  voltage  and  output

will  vary  with  the  field  strength,  which  in  turn  varies  with  the  exciting

current,  and  with  the  motor  field  maintained  at  constant  strength  by  the

exciter,  the  speed  of  the  motor  will  vary  almost  in  direct  proportion  to  the

generator  voltage,  and  the  motor  torque  in  direct  proportion  to  the  current

passing  from  the  generator  to  the  motor.  With  this  system,  the  reversal  of

drive  is  effected  by  reversing  the  direction  of  current  flow  through  the

generator field.

MODIFIED WARD LEO NARD CONTROL SYSTEM

For  application  in  the  traction  or  transportation  field,  certain

modifications  have  been made  in the  original  Ward  Leonard  system.  In  the

first  place,  the  field  polarity  of  the generator  is  not  changed,  and reverse  is

achieved  by  reversing  the direction  of  current  flow through the  field  coils  of

the motor.

The  motor  moreover  is  a  series  motor,  as  generally  employed  for

traction  purposes.  Generator  speed  being  constant,  the  torque  load  on  the

engine varies with the excitation of the generator field and the current output

of the generator.

In  some  cases,  the  separately  excited  field  coil  is  supplemented  by  a

differential  series  field  coil,  that  is,  a  coil  through  which  the  main  current

from the generator flows, but in such a direction that it tends to demagnetize

the  filed.  This  differential  series  field  is  so  proportioned  with  the  engine

running  at  its  normal  speed,  and  the  throttle  wide  open,  the  generator

supplies its f ull load current at the normal emf to the motor.

Vehicle speed can be controlled manually by means of a rheostat in the

exciter circuit, and the differential series field automatically takes care of any

change in traction resistance. For instance, if the vehicle encounters a grade,

it  will  slow  down,  and  so  will  the  motor,  which  is  geared  to  it  directly.  An

increased  current  then  flows  from  generator  to  motor,  but  this  increased

current, passing through the differential series field coil, weakens the field of

the  generator,  thereby  reducing  the  voltage  of the  generator  and  limiting  it

output.  As  the  generator  field  is  weakened,  the  engine  speeds  up,  and  at

higher  speeds  the  engine  generates  more  power,  which  takes  care  of  the

increased load due to the grade.

In the design of such drives, the aim is so to proportion the two source

of the field excitation that as the current output of the generato r increases in

a certain proportion, the generator voltage drops in the inverse proportion, so

that  the output remains constant. If  this object  is attained,  then the  electric

drive  can absorb  the maximum  engine  power  under all driving  conditions, if

necessary.  Engine  output  and  vehicle  speed  can  always  be  controlled  by

means of rheostat in generator field.

ELECTRIC DRIVE FOR BUSES

Electric drive systems generally consist of shunt wound generators and

series wound motors. However, the generator field may be provided also with

a so-called teaser winding, through which current from the car battery flows

for  a  short  time,  while  the  engine  is  being  accelerated.  A  differential  series

wounding may also be used, but it is generally omitted.

The generators and the motors are always provided with commutating

poles,  to  make  possible  sparkles  commutation.  The  reason  for  the  teaser

winding is  that a conventional  shunt wounding  generator, when speeded up,

picks up voltage gradually, and with such a generator there is a tendency for

the engine to “race” when the accelerator pedal is depressed.

With the  teaser  winding, the  full  voltage  of  the car battery is applied

as  soon  as  the  accelerator  is  depressed  beyond  the  idling  position;  hence

generator  field  strength  and  voltage  build  up  rapidly.  As  the  engine  gains

speed, the teaser circuit is interrupted automatically by a switch actuated by

a relay connected across the generator mains.

ADVANTAGES OF ELECTRIC DRIVE

1.  In  the  bus  field  the  electric  drive  replaced  a  conventional  geared

transmission, over which it had certain operating advantages.

2.  It afforded continuous acceleration throughout the entire speed range,

and the shocks sometimes experienced in a bus with mechanical  drive

when resuming after a gear change were eliminated. Such shocks were

particularly annoying  to  passengers who had  just entered and  not yet

seated. Passengers, generally, therefore preferred the electric drive.

3.   Another advantage was greater ease of operation. In city operation the

driver  of  a  bus  had  to  make  several  thousands  gear  changes  a  day,

each  shift  preceded  by  disengagement  of  the  clutch  against  a  spring

pressure  of the  order of  50  lb.  With  electric  drive  there  were no  such

tiring  operations,  consequently  the  driver  was  less  fatigued,  and

accident hazards were said to be reduced.

4.  As  all of  the engine  power  was  absorbed by  the generator,  which was

connected directly to  the  engine,  there  was  no  torque  reaction  on  the

frame, and the power plant could have a very flexible mounting, which

reduced noise and vibration in the bus.

5.  Electric  drive  also  eliminated  both  the  exhaust  fumes,  which

frequently  annoyed passengers  when a  gasoline  bus  was  brought to a

stop and the smoky exhaust of the diesel engine when operating at low

speed  under  heavy  torque  load.  The  fumes  were  due  to  incomplete

combustion  occurring  when  the  throttle  was  closed  and  the  engine

driven  by  the  vehicle,  and  diesel  exhaust  smoke  was  eliminated  or

least  reduced  because  with  electric  drive  the  engine  speed  is  not

reduced in direct proportion to bus speed.

LIMITATIONS OF ELECTRIC DRIVE

1.  Excessive weight of the equipment, high production cost, and relatively

low efficiency over the greater part of the speed range.

2.  With the introduction of hydraulic torque converter drives, which were

much  lighter,  less  expensive  to  produce,  and  more  efficient,  electric

drive disappeared from bus field.

PERFORMANCE CHARACTERISTICS OF ELECTRIC DRIVE

When the vehicle encounters increased resistance to motion, the motor

is pulled down in speed, develops less counter-electromotive force, and draws

more current. Since the current can come only from the generator, the output

of  the latter will  be  similarly increased. In fact,  the  current  received  by  the

motor is exactly the  same as that delivered  by  the generator, except  for  the

small amount required for the generator shunt field.

If  the  field  strength  were constant,  generator voltage  would be

directly  proportional  to  armature  speed,  and  generator  current  to  torque

impressed on the generator armature in excess of that necessary to overcome

bearing and brush friction. But the field strength is not constant in either the

generator or the motor.

The motor has a series field winding, and if its armature current

increases,  the  current  through  its  field  coils  increases  equally.  Therefore,

since  more  torque  is  proportional  to  both  armature  current  and  strength  of

magnetic field, it always increases faster than armature current, and a curve

of motor torque with respect to current flow is convex toward the current axis

over the range of currents corresponding to normal loads.

The  exact  opposite  holds  in  the  case  of  generator.  Field

excitation  of  the  generator  is  derived  from  the  shunt  winding  connected

across  the  generator  means.  When  the  current  delivered  by  the  generator

increases  there  is  an  increase  in  potential  drop  in  armature  windings,  and

consequently  a  decrease  in  terminal  voltage  and  in  field  excitations  due  to

shunt coils.

Hence  even  if  the  generator  speed  remained  absolutely  constant,  the

field  strength  would  decrease  with  an  increase  in  armature  current.

However,  with  increased  torque  load  on  the  engine  due  to  the  greater

armature  current,  the  engine  speed  will  drop,  which  results  in  a  further

decrease in terminal voltage and in field strength.

Thus there is an inherent tendency  for the field strength  of the

generator to decrease  with an increase in armature current. The horsepower

output of the generator is proportional to the product of voltage and current,

and  if  the  generator  voltage  drops  while  the  current  increases,  there  is  a

tendency  for  the  engine  load  to  remain  constant  regardless  of  rear  axle

torque. If this tendency is not sufficiently pronounced it can be strengthened

by providing the generator with the small reverse series winding which tends

to demagnetize the field.

CURVES OF GENERATOR INPUT TORQUE AND MOTOR TORQUE

vs. ARMATURE CURRENT

This  automatic  change  in  the  ratio  of  torque  conversion  by  the

electrical system is well illustrated in figure, which represents torque curves

of generator input (engine torque) and of motor output. It will be noticed that

with a current flow of  120 amps the generator torque  is about 220 lb-ft, and

that  there  is only little variation in the generator  torque from  this point on,

the maximum value being a little more than 250 lb-ft. on the other hand, the

motor  torque,  which  is  about  85  lb-ft  with  a  current  flow  of  120  amps,

becomes  410  lb-ft  with  a  current  flow  of  400  amps.  Thus  at  120  amps,  the

torque is decreased as it would be with a mechanical overdrive having a ratio

of 0.385:1.00,  while at  400 amps,  when the generator torque is 230 lb-ft, the

torque  is  multiplied  the  same  as  with  a  mechanical  reduction  gear  with  a

ratio of 1.78:1.00. At 400 amps, therefore, the torque conversion ratio is about

4.6 times as great as at 120 amps.

CURVES OF GENRATOR SPEED  AND MOTOR SPEED vs.

ARMATURE CURRENT

The  variation  of the  generator  and motor  speeds  with  current  flow  is

shown in figure. It will be seen that generator speed is nearly constant over a

wide range of  current flow, from which it follows that with electric drive the

engine runs at nearly constant speed.

Moreover, with both the  speed  and the  torque  of the  engine output  is

practically constant under  all  operating conditions.  The  motor  speed, on  the

other  hand,  varies  inversely  as  the  motor  torque,  high  motor  speed,

corresponding  to  a  small  current  and  a  low  motor  torque,  and  low  motor

speed to high motor torque.

SEPARATE EXCITATION

When  it  was  first  attempted  to  connect  a  vehicle  motor  directly  to  a

generator driven by a combustion engine without having a battery floating on

the line, one difficulty that was experienced was that when the driver opened

the  throttle  quickly  for  a  rapid  get-away,  engine  would  be  momentarily

without  adequate  load  and  would  “race”  which  not  only  injurious  to  its

mechanism,  but  resulted  in  unpleasant  vibration.  This  difficulty  was

overcome  by  providing  a  certain  amount  of  separate  excitation,  the  current

for  which, must come from a battery. The  teaser current from the  battery  is

kept  flowing  for  a  short  time  only,  until  the  voltage  across  the  generator

mains  has  built up  sufficiently,  and thereafter the  generator  is  self-excited.

Interruption  of  the  teaser  current  is  brought  about  by  a  cut-out  are  teaser

relays. If the teaser cut-out is provided with a shunt coil and a series coil, the

time the teaser coil continues to carry current depends not only on the rate at

which the generator is accelerated, but also on the load it carries.

ELECTRIC BRAKES

When there is no direct mechanical connection between the engine and

the driving wheels, the engine cannot be used as a brake. The electric motor,

however,  lends  itself  to  the  same  purpose.  It  can  be  used  either  as  a  mild

brake,  to  prevent  the  bus  from  attaining  too  high  a  speed  in  descending

grades,  or  as  a  severe  brake,  for  emergence.  In  the  first  case  the  motor  is

merely  disconnected  form  the  generator  and  its  circuit  is  closed  through  a

resistance.  The  braking  power  of  an  engine  can  be  varied  by  means  of  the

throttle. Ordinarily however, only one step is provided. Emergency braking is

effected by connecting the motor to the generator in reverse, with a resistance

in  circuit. The  braking  effect  then  depends  on  the throttle position, and  can

be controlled by means of the throttle.

UNIT V

AUTOMATIC TRANSMISSION APPLICATIONS

CHERVROLET TURBOGLIDE TRANSMISSION

This is a combination of a converter and an epicyclic gear and is shown

in  figure.  The  converter  has  five  elements,  the  pump  P,  three  turbines  or

driven elements T1, T2 and T3, and a reaction member R. The latter is free to

rotate in the forward direction on the freewheel F1 and is provided with a set

of  blades  B,  whose  angles  are  adjustable;  the  mechanism  for  making  the

adjustment is not indicated.

The first turbine element T1 is coupled by the shaft D to the sun S2 of

the second epicyclic train; the second turbine T2 is coupled through the sleeve

E  to  the  annulus  A1  of   the  first  epicyclic  train  and  the  third  turbine  T3  is

coupled  to  the  output  shaft  H  by  the  sleeve  G1,  the  clutch  C1  (which  is

always engaged except when neutral and reverse are selected), the sleeve G2

and the planet carrier R2.

The sun S1 is normally prevented from rotating backwards by the free

wheel  F2, since usually  the clutch C2  is engaged and  the member  K is fixed

so  that  the  sleeve  J  cannot  rotate  backwards.  The  annulus  A2  is  also

prevented  from  rotating  backwards  by  the  freewheel  F3  which  locks  it  for

such rotation to the sleeve J. Engagement of the clutch C3 fixes the annulus

A2  against  forwards  or  backwards  rotation,  and  this  is  done  when  ‘low’  is

selected  so  as  to  reduce  the  load  on  the  freewheel  F3,  when  the  engine  is

pulling  hard  under  adverse  road  conditions,  and  to  allow  the  engine  to  be

used effectively as a brake on down gradients.

At  low  forward  speeds  of  the  output  shaft  H  relative  to  the  engine

speed, the sun S1, and annulus A2  will be stationary because the torques on

them will tend to make them rotate backwards and this motion is  prevented

by  the  freewheels  F2  and  F3.  Both  epicyclic  trains  then  provide  speed

reductions and torque increases, and all three turbines will be driving.

As  the output speed rises,  the torque passing through  the sun  S2 will

fall and at some point will tend to become negative, and then the annulus A2

will  start  to  rotate  forwards  and  the  turbine  T1  will  be  effectively  out  of

action.  At  a  higher  output  shaft  speed,  the  sun  S1  will  start  to  rotate

forwards  and  the  turbine  T2  will  go  out  of  action.  The  drive  will  then  be

through  T3  direct  to  the  output  shaft,  the  only  torque  magnification  then

being that due to the torque converter itself.

Finally,  the  reaction  member  R  will  start  to  rotate  forwards  and  the

torque  converter  will  run  as  a  fluid  coupling.  The  speeds  and  torques  at

which these events occur will depend on  the angle at which the  blades B are

set.

Reverse is obtained by engaging the clutch C4 and disengaging C1, C2

and C3. The trains 1 and 2 are then compounded and give a reverse ratio, the

whole  of the driving torque being transmitted by the turbine T1 and sun S2.

Forward  motion  of  S2  tends  to  drive  R2  forwards  and  A2  backwards;

backward motion of A2, however, results  in backward motion of S1  (through

the free wheel F3 and the sleeve J) and so in train 1, whose annulus is fixed,

the  sun  tends  to  rotate  the  planet  carrier  R1  backwards.  The  backward

torque on R1  is  greater than  the forward torque  on R2 (from S2), and  so  R1

and R2 will move backwards.

CHEVROLET POWERGLIDE TRANSMISSION

Chevrolet  power  glide  transmission  comprises  of  a  three-element

hydraulic torque converter and a two-speed and reverse planetary unit.

CONSTRUCTION

TORQUE CONVERTER

The  impeller  and  runner  are  of  fabricated  construction,  and  have  31

and 33 vanes, respectively.  Their  pressed-steel vanes  have  tabs that fit into

slots in the shells, and after assembly the tabs are spun flat to hold the parts

together.  The  cast  aluminum  reactor  has  12  vanes  of  hydrofoil  section  cast

integral with  the hub,  and  a  wide ring of concave section welded to the ends

of the  vanes.  The reactor is  mounted on an over  running  clutch of the  roller

type. The torque ratio of the converter at stall is 2.10:1

PLANETARY GEARBOX

By  providing intermediate  gears  between  the sun gear  and  planetary

gears  meshing with  a ring  gear,  it  is  possible  to  use the  same sun  gear  and

the same planetary gears for both the low forward speed and the reverse, and

this  arrangement  is  used  in  automatic  transmissions  incorporating  a

hydrodynamic torque converter.

Reverse

Band 2

R

Band 1

Low

Reverse

Gear

C

Planet

High

Carrier

P

1

S

1

S

2

Sun

OUTPUT

INPUT

Gear

SHAFT

SHAFT

Reaction

Gear

Pc

Intermediate

Gear

Band 1

Band 2

Two small adjacent gears are carried on the driving shaft-a driving sun

gear splined thereon. The reaction gear can be held from rotation by means of

a friction band. Three planetary gears mesh with both the ring gear and the

reaction  gear,  and  three  intermediate  gears  of  slightly  more  than  the

combined face  width  of  sun  gear  and  reaction  gear  mesh  with both  the  sun

gear and planetary gears.

OPERATION

For  low  speed  the  reaction  gear  is  held  from rotation by means of  its

friction  band.  The  sun  gear,  which  is  supposed  to  turn  left-handedly  as

indicated  by the  arrow, will turn  the intermediate gears  right-handedly and

the  planetary  (or  reverse)  gears  left-handedly  around  their  respective  axes.

The  planetary  gears  then  roll  on  the  reaction  gear  and  carry  the  planet

carrier--the driven member–along with them; hence the driven member turns

in the same direction as the driving shaf t, but at a  reduced speed. While the

assembly  is  being used as a low-speed forward gear the ring  gear  turns idly

in the same direction in which the sun gear and planet carrier are turning.

For  direct  drive  the  reaction  gear  is  locked  to  the  driving  shaft  by

means  of  a  multiple-disc  friction  clutch.  As  the  two  central  gears  are  then

locked together, it is impossible for the planetary gears to turn on their studs,

and the whole assembly rotates as a unit.

For  reverse  motion  the  ring  gear  is  held  from  rotation  by  its  friction

band.  The  sun  gear,  turning  left-handedly,  rotates  the  intermediate  gears

right  handedly  and  the  planetary  or  reverse  gears  left-handedly,  and  the

later, rolling on the ring gear, carry the planet carrier along with them in the

right-hand direction,  or  in the  direction  opposite to  that  of  the sun  gear.  At

the  same  time  the reaction  gear, which is  now released  by  its friction  band,

idles in the direction in which the planet carrier turns.

When  the  driver  sets  the  selector  lever  in  Drive  and  depresses  the

accelerator pedal, the car will start in low gear, and at a speed determined by

the movement of the accelerator pedal will automatically shift into High gear.

The selector lever has five positions: Park, Neutral, Drive, Low, and Reverse.

To  get  the  lever  into  the  park  position,  it  must  be  lifted  above  its  normal

level, and to get into Reverse it must be lifted over a stop.

GEAR RATIOS

First Gear    :  1.82  : 1

High Gear    :          1 :  1

Reverse Gear  :  1.82  : 1

CLUTCH HYDRAULIC ACTUATION SYSTEM

An  alternative  and  convenient  method  of  transmitting  force  and

movement  is  by  forcing  fluid  through  a  flexible  plastic  pipeline  running

between the foot-pedal and the clutch bell housing.

Controlled clutch action is achieved by having a master- cylinder bolted

to the bulk head and a push-rod connecting the clutch-pedal movement to the

sliding piston. A second cylinder and piston-known as the slave-cylinder unit-

are located and supported on an extension formed on the bell-housing flange.

The  piston  inside  this  cylinder  conveys  the  slightest  movement  to  the  fork-

lever  through  the  slave  push  rod.  The  fork-lever  has  the  thrust-bearing

assembly  attached  to  one  end,  and  a  spherical  pivot  is  situated  slightly  in

from this end.

When  the clutch pedal  is depressed, the  master-cylinder  piston moves

forwards  and  pushes  a  continuous  column  of  fluid  through  the  pipeline.

Consequently,  an  equal  volume  of  f luid  must  be  displaced  into  the  slave-

cylinder so that the piston moves out and tilts the fork-lever. The net result is

that the trust bearing defects the release-fingers so that the driven-plate will

slip.

Engagement of the clutch occurs when the pedal is released-this allows

the fluid to return to the master-cylinder and its reservoir. The return-spring

in the slave-cylinder will then maintain a slight pressure on the fork-lever, so

that the trust bearing will always be in contact with the release-fingers.

Driven-plate  wear  will  be  compensated  for  by  the slave  return-spring

and piston  automatically moving out  to  take  up the increased  fork-lever tilt.

When  subjected to large  leverage  forces,  hydraulic  actuating mechanisms do

not  suffer  f rom  frictional  wear,  as  do  cables.  This  makes  them  particularly

suitable for heavy-duty applications on large trucks.

TOYOTA “ECT-i” A NEW AUTOMATIC TRANSMISSION

WITH INTELLIGENT ELECTRONIC CONTROL SYSTEM

In  recent  years  since  the  oil  crisis,  technological  developments  for

automatic transmissions have been aimed mainly at the improvement of fuel

economy,  with  emphasis  placed  in  increasing  the  efficiency  of  the  complete

power transmission system,  including the  engine.  The four-speed  automatic

transmission,  the  lock-up  clutch  and  their  electronic  controls  have  been

developed  and  their  electronic  controls  have  been  developed  and  put  into

practical  application.  Currently,  efforts  are  being  made  to  increase  the

number  of  transmission  speeds  for  further  improvement  of  drivability  and

power performance.

The  level  of  vehicle  performance  required  by  drivers  is  also  becoming

higher  and  higher.  In  automatic  transmissions  higher  quality  levels  are

required  not only for fuel  economy  and power performance but also  for  shift

quality  noise  reduction,  etc...  Consequently,  smoothness  and  quietness

including  proper  controls  for  the  increased  number  of  gear  shift  operations

required  with  the  increase  in  transmission  speeds  are  major  transmission

developments.

SPECIFICATIONS OF THE TOYOTA ECT- i TRANSMISSION

S.NO.  SPECIFICATIONS  VALUES

1  Torque Capacity  3.6 kg-m (353 N-m)

3-Element, 2-Phase with Lockup

2  Torque Converter

Clutch Type,   Impeller Diameter

272mm.

1

2.531:1

st

Gear Train

2

1.531:1

nd

3

3

1.000:1

rd

Gear Ratio

O.D            0.705:1

Reverse     1.830:1

6 Disc Clutches

4  Friction Element

1 Band Clutches

5  Shift Positions  6 Positions

P-R-N-D-2-3

Electronic Hydraulic Control

19 Valves

6  Control System

2 ON-OFF  Solenoids

2 Linear Solenoids

Automatic

7

Capacity 8.3 liters

Transmission Fluid

8  Weight  77 kg (755 N)

Under  such  circumstances,  TOYOTA  has  developed  a  new  automatic

transmission, called the  A341E.  This transmission employs  a unique engine

and transmission integrated intelligent control  system. The main function of

the engine and transmission integrated intelligent control system are engine

torque  control  and  clutch  hydraulic  pressure  control.  And  the  “super  Flow”

Torque  converter  has  a  modified  geometry  optimized  by  the  analysis  of

internal  flow  by  means  of  computer  simulations,  attaining  the  highest

efficiency  in  the  world.  With  the  use  of  such  systems,  this  new  automatic

transmission has attained very smooth shift changes over system life.

ENGINE AND TRANSMISSION INTEGRATED INTELLIGENT

CONTROL SYSTEM

NEW GENERATION CLUTCH HYDRAULIC ACTUATION SYSTEM

Traditionally  manual  clutch  actuation  for  automobiles  was  a  spin-off

from  hydraulic  brake  technology  namely  heavy  steel  or  cast  iron  cylinders,

steel  pipes  and  rubber  hoses.  Because  of  this  archaic,  inefficient  and

expensive  approach  to  providing  a  mechanical  advantage,  an  alternative

lower  cost  system  of  cable  operation  gained  popularity  throughout  the

industry.  However,  the  1:1  ratio  of  a  cable  plus  routing  problems,  NVH

issues,  efficiency  losses  and  the  need  for  complex  adjustment  mechanisms,

opened up the opportunity for a rebirth of the old hydraulic concept.

The  goal  was  to  design  a  system  with  a  totally  new  approach  that

would  meet  the  following  criteria,  high  efficiency,  increased  temperature

resistance,  increased  durability,  reduced  packages  size  and  weight,  cost

competitive  with  cable  systems,  and  finally  to  take  advantage  of  the  latest

advances in materials and processes.

TWO MARKS QUESTIONS

UNIT I   CLUTCH AND GEARBOX

1. What are the requirements of a transmission system?

2. State the principle of friction clutch.

3. What are the various components of a clutch?

4. What are the requirements of a clutch?

5. What is the necessity of providing clutch free pedal play?

6. Why are coil springs installed in  a clutch plate? (Or) Indicate the function

of the clutch   damper spring.

7. What are the various materials used in the manufacture of clutches?

8. What are the various components of the transmission system?

9. Why are clutch friction plate perforated?

10. List out the various types of clutches used in practice.

11. What are meant by wet and dry clutches?

12. Define clutch grab and clatter.

13. Mention the advantages of diaphragm spring clutch.

14. Write a note on clutch plate materials.

15. Explain the reasons for using cones as engaging surface in a cone clutch.

16.  Why  are  wet-type  of  multi  plate  disc  clutch  preferred  in  automatic

transmission?

17. What are the various materials in which a gear box is made?

18. What are the various types of lubrication available in practice?

19. State different types of gear boxes used in practice?

20. What are the advantages of gear ratios forming geometrical series?   (Or)

Why the gear ratios are arranged in geometrical progression?

21. What is the principle of a synchromesh gear box?

22. What are the advantages of using a spur gear?

23. What is the purpose of gear box in a transmission system? (Or)

State the function of a gear box?

24. What do you mean by the term “speed synchronizing”?

25. What are the different faults found in a gear box?

26. List out the various materials used for the manufacture of gears?

27. Sketch a three speed constant mesh gear box?

28. Mention few materials used for transmission shafts?

29. Discuss the performance curves of a gear box?

30. Sketch 3-speed constant mesh gear box?

31. What is the function of synchronizer?

32.  Find  out  the  axial  force  required  to  synchronize  the  speeds.    Given

coefficient  of  friction  =  0.04,  cone  angle  is  10  degree,  angular

acceleration is 50  rad/sec²,  moment of  inertia  254 kg cm²  and the mean

radius of the cone surface 4.13 cm.

UNIT II   FLUID COUPLING AND TORQUE CONVENTER

1. What are the advantages of the fluid coupling?

2. Define torque capacity?

3. State the principle of torque conversion?

4. State a few advantages of poly phase torque converters?

5. Diff erentiate clearly between a torque converter and a fluid coupling?

6.  Elucidate  three  main  differences  between  fluid  coupling  and  torque

converter.

7. Define slip in a fluid coupling.

8. What is the function of the reaction member in the torque converter?

9. What do you mean by coupling point in two phase torque converter?

10.  Draw  the  polar  diagram  illustrating  the  principle  of  hydro  dynamic

torque conversion.

11. What are the various means used to reduce drag torque in fluid coupling?

12. What are the limitations of fluid coupling?

13. What is the function of a torque converter?

14.  What  are  the  advantages  of  hydraulic  transmission  drives  over  other

drives?

15. What are the limitations of hydrodynamic torque converter?

16. What is the effect of slip in coupling?

17. Discuss the performance characteristics of fluid coupling

18. What is a converter- coupling?

19. What is multistage and poly phase torque converters?

20. What is meant by drag torque?

21.  A  petrol  engine  develops  10  N-m  torque  at  maximum  BHP  speed  of

4000rpm. Determine the diame ter of the impeller required to transmit the

torque for a slip of 3%.

22. Mention the properties to be satisfied for the working fluid used in hydro

dynamic drive.

UNIT III   AUTOMATIC TRANSMISSION

1.  What  are  the  disadvantages  of  Automatic  Transmission  when

compared to conventional transmission?

2.  What are the various parts of an Automatic Transmission System?

3.  What are the advantages of overdrive?

4.  In a gear  system, the front unit having internal  gear of 67 teeth and

run gear of 30 teeth. Find the gear ratio.

5.  What  is  the  function  of  an  over-  running  clutch  in  an  over-  drive

transmission?

6.  Why is locking device necessary for over running clutch in over drive?

7.  How are different speeds obtained in a planetary gear box?

8.  How is reversing achieved in a planetary gear set?

9.  List out any three merits of an automatic transmission.

10. What  are the  advantages of  the epicyclic hear box  over  the ordinary

gear box?

11. What  are  the  relative  merits  of  Automatic  Transmission  when

compared to conventional transmission?

12. In  epicyclic  box  to  get  forward  speed  and  reverse  speed  normally

which member is fixed?

UNIT IV    HYDROSTATIC DRIVE AND ELECTRIC DRIVE

1. What are the advantages and limitations of Electrical drive?

2. What is the various hydraulic transmission drives used in practice?

3. What are the advantages of hydrostatic drives?

4. Differentiate  clearly  between  a  hydrodynamic  and  hydrostatic  drive

systems

5. Draw the  curves  of generator  input torque  and  motor  torque  versus

armature current

6. What  is  the  principle  of  electric  torque  conversion  on  an  electric

drives?

7. What  are the differences in early and later ward Leonard systems of

control?

8. What are the disadvantages of hydrostatic drives?

9. Explain the need for providing a foot switch operated additional field

resistance in the generator field of a modern electric drives for buses

10. Sketch  the  efficiency  and  torque  characteristics  for  hydrostatic

drives having fixed displacement pump a variable motor.

11. Sketch  the  efficiency  and  torque  characteristics  for  hydrostatics

drive  having  variable  displacement  pump  a  fixed  displacement

motor.

UNIT V   AUTOMATIC TRANSMISSION APPLICATIONS

1.

What are the functions of intelligent electronic control system of Toyota

transmission?

2.

Brief about the controls  used  in Toyota ECT-i automatic    transmission

with intelligent control system.

3.

Write a note on new generation hydraulic actuation system of a clutch?

MODEL QUESTION PAPER

B.E. AUTOMOBILE ENGINEERING

SEMESTER V

AT 335 - AUTOMOTIVE TRANSMISSION

Time:  3 Hours              Max. Marks:  100

Answer ALL Questions

PART – A       (10 x 2 = 20 Marks)

1.  What are the requirements of a transmission system?

2.  Explain the reasons for using cone as engaging surface in cone clutch.

3.  Describe the procedure for arriving of suitable gear ratios for Tractors.

4.  Differentiate Torque Converter and Fluid Coupling.

5.  How the torque ratio of a torque converter varies with speed ratio?

6.  Compare the performance characteristics of  different hydraulic pumps

and hydraulic motors combinations.

7.  List out the merits and demerits of Hydrostatic drive.

8.  What are the advantages and limitations of electric drive?

9.  Explain Automatic and Semi-Automatic transmission.

10.  Write a brief note on Automatic Overdrive.

PART – B          (5 x 16 = 80 Marks)

11.   Sketch  the  Wilson  planetary  gearbox.    Explain clearly  how  the  third

gear ratio is obtained for this gearbox.

12. a)  Explain the construction and operation of diaphragm spring

clutch with a neat sketch.

(OR)

12. b)i) Sketch and explain the variation of Tractive effort with vehicle speed.

ii) Explain the necessity of gearbox for a vehicle using performance curves

analysis.

13.a)  Differentiate Multistage and Poly phase torque converter.

Sketch and explain the performance characteristics for the above two

types of torque converters.

(OR)

13.b)  Sketch and explain WHITE’s hydro torque drive.

14.a)  Explain the Janny hydrostatic transmission with a sketch.

(OR)

14.b)  With a circuit diagram explain the operation of Electric drive f or

city buses.

15.a)    With a basic hydraulic circuit diagram, explain the functions of

various valves while engaging second gear.

(OR)

15.b)  Describe Chevrolet ‘Turbo glide’ automatic transmission system.

* * * * *

E 170

813

B.E./B.Tech. DEGREE EXAMINATION, NOVEMBER/DECEMBER 2003.

Fifth Semester

Automobile Engineering

AT 335 — AUTOMOTIVE TRANSMISSION

Time: Three hours

Maximum : 100 marks

Answer ALL the questions.

PART A — (10 × 2 = 20 marks)

1.  What are the requirements for an automotive clutch?

2.  With a sketch illustrate the principle of friction clutch.

3.  Draw the layout of sliding mesh gear box.

4.  What  Find  out  the  axial  force  required  to  synchronize  the  speeds.    Given

coefficient  of  friction  =  0.04,  cone  angle  is  10  degree,  angular  acceleration  is  50

rad/sec², moment of inertia 254 kg cm² and the mean radius of the cone surface 4.13

cm.

5.  A petrol engine develops 10 N-m torque at a maximum BHP  speed of  4000rpm.

Determine the diameter of the impeller required to transmit the torque for a slip of

3%.

6.  What is meant by drag torque? Explain a method of minimizing it?

7.  How the efficiency of a torque converter varies with speed ratio?

8.  What  are  the  different  types  of  hydrostatic  transmission  combination?  Specify

the features of them.

9.  Write a note on new generation hydraulic actuation system of a clutch?

10. List out the merits and demerits of electric drive.

PART B — (5 × 16 = 80 marks)

11. The b.p of a vehicle is 94.2 kW at 3300 rpm. The total tractive resistance on low

gear including gradient resistance is 5395.5 N and that in the top gear is 1697

N.  the  diameter  of  the  wheels  is  0.9144  m  and  the  efficiency  of  the

transmission is 75% on low gear and 85% in top gear. Calculate the gear ratio

for a three-speed gear box.

12. (a)  Explain  the  principle  of  operation  of  hydrodynamic  fluid  coupling  with

relevant sketch.

Or

(b)  Explain the principle of operation of hydrodynamic torque converter with a

polar diagram.

13.  (a)  Explain how second gear is obtained in Wilson gear box with a neat sketch.

Deduce the second gear ratio.

Or

(b)  How  shift valves  are  controlled  by throttle  and governor valves  / with  a

hydraulic circuit explain how second gear is engaged?

14. (a)  Describe Janny hydrostatic transmission system with a neat sketch.

Or

(b)  Explain the principle of modified ward Leonard type of control for electric

drive in vehicles.

15. (a)  Explain the construction and operation of single plate diaphragm spring

clutch with a neat sketch.

Or

(b)  Explain  Chevrolet  ‘turbo  glide’  automatic  transmission  system  with  a

sketch.

_____________________

K 1007

170 813

B.E./B.Tech. DEGREE EXAMINATION, NOVEMBER/DECEMBER 2004.

Fifth Semester

Automobile Engineering

AT 335 — AUTOMOTIVE TRANSMISSION

Time: Three hours

Maximum: 100 marks

Answer ALL the questions.

PART A — (10 × 2 = 20 marks)

1.  Enumerate the various requirements t be satisfied by a clutch.

2.  What are the main functions to be performed by the vehicle transmission

system?

3.  Write the requirements to be satisfied by automatic transmission fluids.

4.  Write the advantages of fluid coupling.

5.  Write the advantages of epicyclic gear system.

6.  What is meant by drag torque and how it can be reduced?

7.  Write the advantages of hydrostatic drives.

8.  Brief about the advantages of electric drives in a automatic vehicle.

9.  Brief about the controls used in Toyota ECT-i automatic transmission with

intelligent control system.

10. write the advantages of diaphragm type of clutch

PART B — (5 × 16 = 80 marks)

11.  A  truck  has  a  gross  vehicle  weight  of  89026  N.  engine  displacement  is

10m

,  power  77.3kW at governed  speed, of  2400  r.p.m.  maximum  torque,

3

345.8 Nm  at  1400r.p.m.  Rear  axle  ratio,  6.166:  1.  fourth speed  reduction

ratio  in  transmission,1.605  :1,  drive  line  losses  amount  to  10.7kW  at

2400r.p.m  and  6.3kW  at  1400r.p.m.type  size  0.4572  m  x1.016m(effective

wheel  diameter  0.950m),frontal  area  of  truck  6.95mcalculate  the  grades

which the vehicle can climb in fourth gear in still air conditions.

(i) At governed engine speed; and

(ii) At speed of maximum torque, in the equation

R = KW +Ka A V²

Ka= 0.0462 where V in km/hr

12.  (a) By using the line sketch explain the working of hydrodynamic torque

converter.

(Or)

(b) Draw graph for characteristics of a conventional three element converter

by using this explain the general properties of the hydrodynamic torque

converter.

13.  (a)  describe  the  working  principle  of  ford  model  T  planetary  transmission

with a suitable sketch.

(Or)

(b)  Explain the  working  principle of Wilson  planetary transmission. Draw

neat line sketch of the system.

14.  (a)  By  using  simple  line  sketch  explain  the  working  of  janney  hydrostatic

drive.                                                (Or)

(b) Describe the working of early ward Leonard control system.

15. (a) Describe the working of Chevrolet turboglide transmission.

(Or)

(b) Describe the construction and working of single plate spring clutch.

---------------

S 202

B.E./B.Tech. DEGREE EXAMINATION, APRIL/MAY 2005.

Fifth Semester

Automobile Engineering

AT 335 — AUTOMOTIVE TRANSMISSION

Time: Three hours

Maximum: 100 marks

Answer ALL the questions.

PART A — (10 × 2 = 20 marks)

1.  What is meant by double deducting?

2.  How clutches are classified?

3.  What is the principle of synchronizing?

4.  What are the differences between fluid coupling and torque converter?

5.  Define slip with respect to torque converter.

6.  State some advantages of hydrometric transmission.

7.  What are hydrostatic transmission combinations?

8.  What is meant by turbo glide?

9.  What is meant by intelligent control?

10. Compare a mechanical clutch with fluids coupling.

PART B — (5 × 16 = 80 marks)

11. In a gear box the clutch shaft pinion has 14 teeth and low gear main shaft pinion

32 teeth. The corresponding lay shaft pinions have 36 teeth and 18 teeth. The

axle ratio is 3.7:1 and effective radius of the rear type is 35.5 cm. calculate the

car speed in the above arrangement at an engine speed of 2500rpm.

12. (a)   (i)discuss various type of gear boxes used in an automobile.   (6)

(ii)  What  is a  synchronizing  device?  How this device  helps smooth  gear

engagement.

(10)

Or

(b)  (i)  What is the functions of a clutch?  (3)

(ii)  Draw  a  neat  sketch  of  a  centrifugal  clutch  and  explain  its

construction and operation.  (13)

13. (a)  What  is  a  fluid  coupling?  Explain  its  constructional  details.  Draw  and

explain its performance curves.  (16)

Or

(b)  Draw  a  neat  sketch  of  a  multistage  torque  converter  and  explain  its

construction and working principle.  (16)

14. (a)  (i) What is meant by automatic drive?  (4)

(ii)Draw a schematic diagram of  hydraulic  control system for  automatic

transmission and explain.

(12)

Or

(b)  (i)  What  are  the  principles  involved  in  hydrostatic  drive?  What  are  it

advantages and limitations?

(8)

(ii) Compare hydrostatic and hydrodynamic transmission.  (8)

15. (a)  Draw a neat sketch of a Chevrolet Turbo glide transmission and explain

its salient features.      (16)

Or

(b)  (i)  Discuss about Toyota ECT-i Transmission.  (8)

(ii)  Discuss about Hydraulic Actuation system.  (8)

——————

J 271

B.E./B.Tech. DEGREE EXAMINATION, APRIL/MAY 2004.

Fifth Semester

Automobile Engineering

AT 335 — AUTOMOTIVE TRANSMISSION

Time: Three hours

Maximum: 100 marks

Answer ALL the questions.

PART A — (10 × 2 = 20 marks)

1. List out the requirements of transmission system.

2. How  engagement  and  disengagement  can  be  affected  in  an  electromagnetic

clutch.

3. What is meant by tractive effort? How is it obtained from engine torque?

4. What is the function of a gear synchronizer?

5. How the torque ratio of a torque converter varies with speed ratio?

6. Compare  the  performance  characteristics  of  different  hydraulic  pump  and

motor combinations.

7. What are advantages and limitations of electric drive?

8. What is the effect of current on variation of torque of an electric drives?

9. What  are  the  functions  of  intelligent  electronic  control  system  of  Toyota

transmission?

10.  A  petrol  engine  develops  13  Nm  torque  at  a  maximum  b.h.p  speed  of

3500rpm.determine  of  the impeller required  to  transmit  it  the  torque  for  a

slip of 3%.

PART B — (5 × 16 = 80 marks)

11.  Explain  Chevrolet  “turbo  glide”  automatic  transmission  system  with  a

sketch.

12. (a)  A motorcar engine develops 5.9 b.k W at2100rpm. Find the suitable size

of  clutch plate having friction  linings riveted on both sides, to transmit the

power, under the following conditions:

(v)  Intensity of pressure on the surface not to exceed 6.87x10  pa.

(vi)  Slip torque and losses due to wear etc. is 35% of engine torque.

(vii)  Coefficient of friction on contact surface is 0.3.

(viii) Inside  diameter  of  the  friction  plate  is  0.55  times  the  outside

diameter.

Also calculate the dimensions of pressure plate.

Or

(b)  The  coefficient  of  rolling  resistance  for  a  truck  weighing  62293.5  N  is

0.018  and  the  coefficient  of  air  resistance  is  0.0276  in  the  formula

R=KW+Ka  AV²,  N,  where  A  is  m²  of  frontal  area  and  V  the  speed  in

km/hr. the transmission efficiency in top gear of 6.2:1 is 90% and that in

the second gear of 15:1 is 88%. The frontal area is 5.574 m². If the truck

has to have maximum speed of88km/hr. in top gear calculate.

(i) the engine b.p required;

(ii) the engine speed  if the  driving wheels have  an effective  diameter  of

0.8125m;

(iii)  The  maximum  grade  the  truck  can  negotiate  at  the  above  engine

speed in second gear.

13. (a)  Explain the principle and operation of fluid coupling with sketches.

Or

(b)  Explain the necessary, construction and operation  of multi-stage torque

converter with a neat sketch.

14. (a)  Explain  how  second  gear  is  obtained  in  Wilson  gear  box  with  a  neat

sketch. Deduce that gear ratio.

Or

(b)  Explain  the  construction  and  operation  of  cotal  electromagnetic

transmission with a sketch.

15. (a)  Describe janny hydrostatic transmission system with a neat sketch.(Or)

(b)  Explain the principle of ward Leonard type of control for electric drive.