## Slide 1
CAST IRON AND STEELS
IDENTIFY MATERIALS AS PER COMPONENT PARTS

## Slide 2
Axles: medium to high c steel with alloying elements Cr, Ni, Co.
Shafts: medium to high c steel with alloying elements Cr, Ni, Co.
Auto part axle shaft
Shaft with universal joint

## Slide 3
Nut bolt assembly
Low to medium carbon steel
Low alloy steel
Gudgeon pin
Medium to high c steel
Medium alloy steel

## Slide 4
Crank shaft
High alloy steel
Alloying elements as
Co, Ni, V, Cr
Connecting rod
Cast steel or stellites
Medium to high c alloy steel

## Slide 5
Water tank
Gray cast iron or
Wrought iron
Manhole cover
Gray cast iron or
Wrought iron

## Slide 6
Shear blades
High c steel
Alloy steel
Milling cutter
Hss- high speed steel 18-4-1
W-Cr-V

## Slide 7
Gear hobs
HSS
bonnet
Low carbon medium alloy steel
Alloying elements Ti, Cr, Co, Mo
car bodies : low carbon low alloy steel

## Slide 8
Bed ways
Gray cast iron
stainless steel
Utensils

## Slide 9
Low grade material axle shaft:
SAE 1541M alloy steel composition consisting essentially of 0.40-0.48% carbon, 1.35-1.61% maganese, 0.16-0.30% silicon, 0-0.23% chromium and the balance iron and other materials not affecting hardenability of the steel, especially adapted for forming axle shafts in the 1.70-2.05" diameter range to be used as drive axles with an axle load carrying capacity between 30,000 and 44,000 pounds.

## Slide 10
Thanks !!!