## Slide 1
SYMBOLS
USED IN
HYDRAULIC & PNEUMATIC CIRCUITS

## Slide 2
BASIC SYMBOLS
-CONTINUOUS LINE - FLOW LINE
DASHED LINE - PILOT, DRAIN
ENVELOPE - LONG AND SHORT DASHES AROUND TWO OR MORE COMPONENT SYMBOLS.
LINES-----

## Slide 3
LARGE CIRCLE
PUMP, MOTOR
small circle
MEASURING DEVICES
semi-circle
ROTARY ACTUATOR
Circular-----

## Slide 4
one square
- PRESSURE CONTROL FUNCTION
-two or three
Adjacent squares: -
DIRECTIONAL CONTROL
Square ----
4/2 DC VALVE
4-PORTS
2-POSITIONS

## Slide 5
FLUID CONDITIONER
(filter, separator, lubricator,
Heat exchanger)
Diamond---

## Slide 6
SPRING
FLOW RESTRICTION
solid -
DIRECTION OF HYDRAULIC FLUID FLOW
open -
DIRECTION OF PNEUMATIC FLOW
Miscellaneous Symbols ----
Triangle---

## Slide 7
Pumps and Compressors----
Fixed Displacement hydraulic pump
UNIDIRECTIONAL
BIDIRECTIONAL
Variable displacement hydraulic pump
UNIDIRECTIONAL
BIDIRECTIONAL

## Slide 8
COMPRESSOR

## Slide 9
UNIDIRECTIONAL
Motors---
FIXED DISPLACEMENT HYDRAULIC
MOTOR
BIDIRECTIONAL

## Slide 10
VARIABLE DISPLACEMENT HYDRAULIC
MOTOR
UNIDIRECTIONAL
BIDIRECTIONAL

## Slide 11
PNEUMATIC MOTOR
unidirectional
bidirectional

## Slide 12
ROTARY ACTUATOR
HYDRAULIC
PNEUMATIC

## Slide 13
-RETURNED BY EXTERNAL FORCE
SINGLE ACTING CYLINDER
RETURNED BY SPRING OR EXTENDED BY SPRING FORCE
-SINGLE PISTON ROD (FLUID REQUIRED TO EXTEND AND RETRACT)
DOUBLE ACTING CYLINDERS
DOUBLE ENDED PISTON ROD

## Slide 14
- SINGLE FIXED CUSHION
CYLINDERS WITH CUSHIONS
DOUBLE FIXED CUSHION

## Slide 15
DIRECTIONAL CONTROL VALVES
NORMALLY CLOSED
DIRECTIONAL CONTROL VALVE
WITH 2 PORTS AND 2 FINITE POSITIONS.
-
NORMALLY OPEN DIRECTIONAL CONTROL VALVE
WITH 2 PORTS AND 2 FINITE
POSITIONS

## Slide 16
Directional control valve (3 ports / 2 positions)
NORMALLY CLOSED DIRECTIONAL CONTROL VALVE WITH 3 PORTS
AND 2 FINITE POSITIONS.
NORMALLY OPEN
DIRECTIONAL CONTROL VALVE
WITH 3 PORTS AND 2 FINITE POSITIONS.

## Slide 17
DIRECTIONAL CONTROL VALVE
(4 PORTS / 2 POSITIONS)
DIRECTIONAL CONTROL VALVE
WITH 4 PORTS AND 2 FINITE POSITIONS
DIRECTIONAL CONTROL VALVE
(4 PORTS / 3 POSITIONS)
DIRECTIONAL CONTROL VALVE WITH
4 PORTS AND 3 FINITE POSTIONS
-(CENTER POSITION CAN HAVE VARIOUS FLOW PATHS)

## Slide 18
DIRECTIONAL CONTROL VALVE
(5 PORTS / 2 POSITIONS)
NORMALLY A PNEUMATIC
VALVE
DIRECTIONAL CONTROL VALVE
WITH 5 PORTS AND 2 FINITE POSTIONS
DIRECTIONAL CONTROL VALVE
(5 PORTS / 3 POSITIONS) NORMALLY A PNEUMATIC VALVE
DIRECTIONAL CONTROL VALVE WITH 5 PORTS AND 3 FINITE POSITIONS

## Slide 19
CONTROL METHODS
MANUAL CONTROL
-LEVER
GENERAL SYMBOL
(WITHOUT SHOWING THE CONTROL TYPE)
PUSHBUTTON
FOOT PEDAL

## Slide 20
MECHANICAL CONTROL
PLUNGER OR TRACER
SPRING
ROLLER(ONE DIRECTION ONLY)
ROLLER

## Slide 21
ELECTRICAL CONTROL
SOLENOID
(THE ONE WINDING)
Pilot Operation
PNEUMATIC
-HYDRAULIC

## Slide 22
PILOT OPERATED TWO-STAGE VALVE
PNEUMATIC:
SOLNOID FIRST STAGE
PNEUMATIC :
AIR PILOT SECOND STAGE
HYDRAULIC: SOLNOID FIRST STAGE
HYDRAULIC:
HYD. PILOT SECOND STAGE

## Slide 23
CHECK VALVES, SHUTTLE VALVES,
RAPID EXHAUST VALVES
CHECK VALVE
-FREE FLOW ONE DIRECTION,
BLOCKED FLOW IN OTHER DIRECTION
PILOT OPERATED CHECK VALVE,
PILOT TO CLOSE
PILOT OPERATED CHECK VALVE,
PILOT TO OPEN

## Slide 24
SHUTTLE VALVE
TO ISOLATE ONE PART OF A
SYSTEM FROM AN ALTERNATE
PART OF CIRCUIT.
RAPID EXHAUST VALVE/PNEUMATIC
INSTALLED CLOSE TO AN
ACTUATOR FOR RAPID
MOVEMENT OF THE ACTUATOR.

## Slide 25
PRESSURE CONTROL VALVES
LINE PRESSURE IS LIMITED TO THE SETTING OF THE VALVE,
SECONDARY PART IS DIRECTED TO TANK.
PROPORTIONAL PRESSURE RELIEF
LINE PRESSURE IS LIMITED TO AND PROPORTIONAL TO AN
ELECTRONIC SIGNAL

## Slide 26
SEQUENCE VALVE
WHEN THE LINE PRESSURE REACHES THE SETTING OF THE VALVE,
VALVE OPENS PERMITTING FLOW TO THE SECONDARY PORT. THE PILOT MUST BE EXTERNALLY DRAINED TO TANK.
PRESSURE REDUCING VALVE
PRESSURE DOWNSTREAM OF VALVE IS LIMITED TO THE SETTING
OF THE VALVE

## Slide 27
FLOW CONTROL VALVES
THROTTLE VALVE
ADJUSTABLE OUTPUT FLOW
FLOW CONTROL VALVE
WITH FIXED OUTPUT (VARIATIONS IN INLET
PRESSURE DO NOT AFFECT
RATE OF FLOW)

## Slide 28
WITH VARIABLE OUTPUT
FIXED ORIFICE
METERED FLOW TOWARD RIGHT
FREE FLOW TO LEFT

## Slide 29
PRESSURE COMPENSATED FLOW CONTROL VALVE FIXED OUTPUT FLOW
REGARDLESS OF LOAD
PRESSURE AND TEMPERATURE
COMPENSATED FCV
FLOW DIVIDING VALVE
FLOW IS DIVIDED EQUALLY TO
TWO OUTPUTS

## Slide 30
SHUT-OFF VALVE
Simplified symbol
ACCUMULATORS
SPRING LOADED
DEAD WEIGHT
GAS FILLED

## Slide 31
FILTERS, WATER TRAPS, LUBRICATORS AND
MISCELLANEOUS APPARATUS
FILTER OR STRAINER
WITH MANUAL DRAIN
WITH AUTOMATIC DRAIN

## Slide 32
FILTER WITH WATER TRAP
WITH MANUAL DRAIN
AUTOMATIC DRAIN
AIR DRYER
REFRIGERANT, OR CHEMICAL REMOVAL OF WATER FROM COMPRESSED
AIR LINE

## Slide 33
LUBRICATOR
OIL VAPOR IS INDUCTED INTO AIR LINE
CONDITIONING UNIT/ FRL UNIT
COMPOUND SYMBOL OF
FILTER, REGULATOR, LUBRICATOR
UNIT
Simplified Symbol
F
R
L

## Slide 34
HEAT EXCHANGERS
AIR OR WATER COOLED UNIT
DESIGNED TO REMOVE HEAT
FROM OIL RETURNING TO RESERVOIR
COOLER
HEATER
HEAT ADDED
TO HEAT OIL

## Slide 35
THANKS !!